## Slide 1
LESSON 3
Bluetooth and Persistent Storage
Allowlists, callbacks, EEPROM that is not EEPROM, and making a vehicle remember which controller is its own.
PORPOISE ROBOTICS - Precision Oceanographic Program On and In the Sea Environment
porpoiserobotics.org
Kevin Bowen, President - kbowen6@icloud.com
Malcom Graham, VP Education Louis Parker, VP Technology
Valen Farre, System Engineer Gary Howland, Animation
Eddie Revollo, Artificial Intelligence
Interns: Oscar Canazales, Krishnansh Vemulapalli, Soham Gangal, Erik Olsen
Three hours. Bring two controllers per group if you can.
Porpoise Robotics - proprietary. For use with Porpoise Robotics lessons.
Notes: Two controllers per group makes the allowlist activity far better. If you only have one each, pair groups up for that section.
Charge every pad before the class. A flat controller looks exactly like a refused connection.

## Slide 2: What you will be able to do by the end
Pathfinder Advanced - Op Program 12 | Lesson 3
1
By the end of this lesson you will be able to:
1. Explain what a callback is and when it runs
2. Configure a Bluetooth allowlist correctly, in the right order
3. Say what EEPROM.commit() actually does on an ESP32, and why it must not be called from loop()
4. Design a storage map with a validity marker, and load it defensively
5. Walk through the full pairing workflow end to end
Notes: Objective three - what commit() actually does - is the one that prevents a real hardware failure later. Do not let it slide by.

## Slide 3: Today, in order
Pathfinder Advanced - Op Program 12 | Lesson 3
2
Time | What we do
0:00 | Recap. Bluepad32, callbacks, and who calls whom
0:25 | The allowlist, and the order the calls must go in
0:50 | Upload a3a_controller_address. Lock and unlock a board
1:20 | BREAK (10 minutes)
1:30 | There is no EEPROM on an ESP32
1:55 | Magic bytes, storage maps, and never trusting storage
2:15 | BREAK (10 minutes)
2:25 | Upload a3b_eeprom_settings. Pull the cable out
2:50 | The full pairing workflow in Op 12
Notes: Two breaks. Both activities are long and both are worth their time.

## Slide 4: Callbacks: functions you write and never call
Pathfinder Advanced - Op Program 12 | Lesson 3
3
Inversion of control
  BP32.setup(&onConnectedController, &onDisconnectedController);
You hand Bluepad32 the ADDRESSES of two of your functions. It calls them when something happens. You never call them yourself.
That inversion is worth naming. Normally your code calls a library. With a callback, the library calls your code. It is how every event system works, from button handlers to network stacks.
The practical question is always: WHEN does it run, and what is safe to do in there?
Here, both callbacks run from inside BP32.update(), which you call yourself from loop(). So they run on your thread, at a moment you chose, and it is safe to print and to touch program state.
If they ran from an interrupt, neither of those would be true.
Notes: Name the inversion out loud: normally your code calls a library, and with a callback the library calls your code.
The practical question is always WHEN it runs and what is safe to do there. Ask that before you answer it.
Here both callbacks run inside BP32.update(), which they call themselves from loop(). So it is their thread, at a moment they chose, and printing is safe.
The last line is the important caveat. From an interrupt, neither of those would be true - and that is a whole category of embedded bug.

## Slide 5: The allowlist, and the two ways to get it wrong
Pathfinder Advanced - Op Program 12 | Lesson 3
4
A guest list, checked at the door
A Switch pad in pairing mode connects to whichever host answers first. Pairing alone does not give you one-vehicle-one-controller.
The allowlist is a guest list checked BEFORE a connection is accepted:
  uni_bt_allowlist_remove_all();
  uni_bt_allowlist_add_addr(address);
  uni_bt_allowlist_set_enabled(true);
Notes: Set the problem up first: pairing alone does not give you one vehicle per controller.
Mistake one is the cruel one. Called before setup(), the allowlist calls do nothing AT ALL, and they do it silently. No error, no warning.
Mistake two is the one that rots slowly: add rather than rebuild, and stale entries accumulate where nobody can see them.
Rebuild from scratch every boot, and the sketch is the single source of truth. That principle is worth stating generally.

## Slide 6: The allowlist, and the two ways to get it wrong (continued)
Pathfinder Advanced - Op Program 12 | Lesson 3
5
MISTAKE ONE: calling them before BP32.setup(). Setup is what brings the Bluetooth stack up. Before that there is no list to add to, and the calls do nothing at all - silently.
MISTAKE TWO: adding to the list instead of rebuilding it. Rebuild from scratch every boot and the sketch is always the single source of truth. Add, and stale entries accumulate where nobody can see them.
Note that enableNewBluetoothConnections stays TRUE. The allowlist keeps other people out; leaving new connections on means your own pad can always get back in even if the bonding keys are lost.
WATCH OUT 11.2 added addresses at runtime only. If those entries did not survive a reboot, a vehicle could come back up with an empty allowlist AND new connections disabled - and then refuse its own controller with no way in.
Notes: (Continued from the previous slide - the same notes apply.)
Set the problem up first: pairing alone does not give you one vehicle per controller.
Mistake one is the cruel one. Called before setup(), the allowlist calls do nothing AT ALL, and they do it silently. No error, no warning.
Mistake two is the one that rots slowly: add rather than rebuild, and stale entries accumulate where nobody can see them.
Rebuild from scratch every boot, and the sketch is the single source of truth. That principle is worth stating generally.

## Slide 7: Where we are
Pathfinder Advanced - Op Program 12 | Lesson 3
6
Callbacks and allowlist
done
Locking a board
NOW
EEPROM
Notes: Twenty seconds. First activity.

## Slide 8: Do it now - lock a board to one pad
Pathfinder Advanced - Op Program 12 | Lesson 3
7
UPLOAD AND RUN: a3a_controller_address (35 minutes)
1. Upload. The allowlist starts OFF. Connect a controller.
2. Type lock. Disconnect, and connect a DIFFERENT controller.
3. Watch the refusal in the Serial Monitor.
4. Type open and try the second one again.
5. Type lockaddr 00:11:22:33:44:55 and try to connect anything.
6. Type whoami. Compare with what a Bluetooth scanner app on your phone shows for this board.
What you should see
Every connection attempt prints an address. With the lock on, everything except the locked address is turned away.
Answer these
Where does this sketch keep its locked address, and what happens to it at the next reset?
Why does the sketch call applyAllowlist() AFTER BP32.setup()?
Notes: Step 3 is the moment it becomes real: a second controller turned away with a printed reason.
Step 5 locks to an address that does not exist, so nothing can connect. Good for showing that the mechanism really is doing the work.
Step 6 cross-checks against a phone scanner app. Worth doing - it connects the number on screen to something outside the room.
Answers: this sketch keeps the address in RAM only, so it is gone at reset; and applyAllowlist() must come after BP32.setup() because setup is what brings the stack up.

## Slide 9: There is no EEPROM on an ESP32
Pathfinder Advanced - Op Program 12 | Lesson 3
8
It is flash, pretending
The EEPROM library is an EMULATION. It reserves a slice of the flash chip, keeps a copy in RAM, and only writes the flash when you call commit().
Three consequences:
  EEPROM.begin(size) must come first, before any get or put.
  Nothing is stored until EEPROM.commit(). Forgetting it is the single most common cause of "my settings did not save".
  Flash WEARS OUT - roughly a hundred thousand erase cycles per sector. Plenty for saving when a human asks. Nowhere near enough to commit() inside loop().
Notes: Lead with the headline: there is no EEPROM on this chip. The library is an emulation over flash.
The three consequences are all practical. begin() first, nothing saved without commit(), and flash wears out.
The warning panel has the arithmetic: a commit() in loop() at 30 Hz burns a hundred thousand cycles in under an hour. Say that number out loud.
The rule to take away: write when something changed and a person asked, never on a schedule.

## Slide 10: There is no EEPROM on an ESP32 (continued)
Pathfinder Advanced - Op Program 12 | Lesson 3
9
Never write on a schedule. Write when something actually changed, and only when a person asked for it.
WATCH OUT A commit() in loop() at 30 Hz burns through a hundred thousand cycles in under an hour.
Notes: (Continued from the previous slide - the same notes apply.)
Lead with the headline: there is no EEPROM on this chip. The library is an emulation over flash.
The three consequences are all practical. begin() first, nothing saved without commit(), and flash wears out.
The warning panel has the arithmetic: a commit() in loop() at 30 Hz burns a hundred thousand cycles in under an hour. Say that number out loud.
The rule to take away: write when something changed and a person asked, never on a schedule.

## Slide 11: The storage map, and why the addresses are spaced out
Pathfinder Advanced - Op Program 12 | Lesson 3
10
Config.h
const int ADDR_DEADZONE = 0; // int, 4 bytes
const int ADDR_DEADZONE_LS_X = 4;
const int ADDR_DEADZONE_LS_Y = 8;
const int ADDR_DEADZONE_RS_X = 12;
const int ADDR_DEADZONE_RS_Y = 16;
const int ADDR_LS_Y_SC = 20; // float, 4 bytes
const int ADDR_LS_X_SC = 24;
const int ADDR_RS_Y_SC = 28;
const int ADDR_RS_X_SC = 32;
const int ADDR_PAIRED_VALID = 36; // 1 byte: 0xA5 when valid
const int ADDR_PAIRED_ADDR = 37; // 6 bytes: the address
const uint8_t PAIRED_VALID_MAGIC = 0xA5;
EEPROM is a flat array of bytes. YOU choose where each value lives, and nothing stops two values overlapping.
An int is 4 bytes and a float is 4 bytes on this chip, so each slot gets 4.
Laying them out as one ADDR_ constant per value, in one place, is what makes an overlap visible when you read the file.
Get this wrong and one setting silently corrupts another. It will look like a hardware fault.
Notes: EEPROM is a flat array of bytes and YOU choose the layout. Nothing stops two values overlapping - the compiler cannot help you here.
Four bytes per slot because an int and a float are both four bytes on this chip.
Ask why the addresses are spaced out and written down in one place. The answer is that a map you can read is a map you can extend safely.
They break this deliberately in step 6 of the activity, so plant the idea now.

## Slide 12: The magic byte, and never trusting storage
Pathfinder Advanced - Op Program 12 | Lesson 3
11
Two separate checks, for two separate problems
A brand new ESP32 has flash full of 0xFF. Read an int out of that and you get -1. Read a float and you get something meaningless.
So the first byte of the block is a MARKER, written only after a successful save. If it is not 0xA5, the data is not ours and we use the compiled-in defaults.
But that is not enough on its own. Even WITH the marker, every value is range checked as it loads:
  if (saved_dz >= 0 && saved_dz <= DEADZONE_MAX) INPUT_DEADZONE = saved_dz;
Why? Because a value saved by an OLDER version of the program is perfectly valid data and still wrong for this one. The marker tells you the bytes are yours. It does not tell you they still make sense.
Defensive loading is not paranoia. It is the difference between a vehicle that boots with odd settings and one that will not boot.
Notes: Start with the fact: new flash is full of 0xFF. Read an int out of that and you get -1.
The magic byte says the bytes are OURS. It does not say they still make sense.
That distinction is the whole slide. A value written by an older version of the program is perfectly valid data and still wrong for this one.
Defensive loading is not paranoia - it is the difference between a vehicle that boots with odd settings and one that will not boot at all.

## Slide 13: Where we are
Pathfinder Advanced - Op Program 12 | Lesson 3
12
Callbacks and allowlist
done
Locking a board
done
EEPROM
NOW
Notes: Twenty seconds. Second activity.

## Slide 14: Do it now - settings that survive
Pathfinder Advanced - Op Program 12 | Lesson 3
13
UPLOAD AND RUN: a3b_eeprom_settings (30 minutes)
1. set deadzone 100, save. Now UNPLUG the board and plug it back in. Type show.
2. set deadzone 200 and do NOT save. Reset the board. What happened, and why?
3. erase, then reset. Where did the values come from this time?
4. dump before and after a save. Find the magic byte.
5. Comment out the EEPROM.commit() in saveSettings. Save, reset, and see the bug you will one day write for real.
6. Deliberately overlap two ADDR_ constants and watch one setting eat the other.
What you should see
Step 1: the value is still 100 after a power cycle. Step 2: it is back to 100, not 200.
Answer these
What is at address 0 in the dump, and what does it mean?
Why is range checking needed even when the magic byte is correct?
Notes: Step 1 involves physically unplugging the board. Make sure nobody is mid-upload when they do it.
Step 5 is the deliberate bug: comment out commit(), save, reset, and watch the setting vanish. That is the mistake they will one day make for real.
Step 6 overlaps two addresses on purpose and one setting eats the other. It makes the flat-array point concrete.
Answers: address 0 holds the deadzone int; and range checking is needed even with a correct magic byte because an older version could have written a value this version cannot use.

## Slide 15: Where each program keeps its controller address
Pathfinder Advanced - Op Program 12 | Lesson 3
14
Four programs in this repository, four different answers, each right for what it is for.
Program | Where the address lives | What that costs you
pathfinder_ps3 | In the CONTROLLER, written by SixaxisPairTool | Needs a Windows PC and a cable to change
pathfinder_nintendoswitch | A constant in the source, MY_CONTROLLER | Recompile to change it
a3a_controller_address | RAM only | Gone at the next reset - fine for a demonstration
Pathfinder_Op_Program12 | EEPROM, written the first time it pairs | Nothing. Press BOOT and pair again.
KEY POINT A field-serviceable machine should never need a laptop to change who is allowed to drive it. That is the whole argument for the EEPROM version.
Notes: Four programs, four answers, and each is right for what it is for. Do not let this become a ranking.
The cost column is where the engineering judgement lives. Read that rather than the middle column.
The note is the argument for the EEPROM version: a field-serviceable machine should never need a laptop to change who is allowed to drive it.

## Slide 16: The pairing workflow, end to end
Pathfinder Advanced - Op Program 12 | Lesson 3
15
Bluetooth.ino
// Two ways in, both do the same thing:
// - press the BOOT button (GPIO 0, reads LOW when pressed)
// - type 'pair' on the serial console
void enterPairingMode() {
// drop whatever is connected
BP32.forgetBluetoothKeys();
clearPairedAddress(); // clears the EEPROM marker
applyAllowlist(); // now empty, so disabled
BP32.enableNewBluetoothConnections(true);
led_mode = PAIRING; // LEDs breathe blue
}
// Then, in the connect callback:
if (!paired_addr_valid) {
savePairedAddress(props.btaddr); // straight to EEPROM
applyAllowlist(); // rebuild, now enabled
}
The first controller to connect during pairing becomes this vehicle's own, and is written down immediately.
applyAllowlist() is called again straight away, so the window where anything can connect closes the moment it is filled.
forget reopens it deliberately.
The LEDs breathing blue is the only feedback a student gets with no laptop attached. That is a deliberate design decision, not decoration.
Notes: Two ways in, one code path. That is a design choice worth pointing at - a button and a console command that do exactly the same thing.
The first controller to connect during pairing becomes the vehicle's own and is written down immediately, not at shutdown.
Ask why it is written immediately. Because a vehicle that loses power before saving would come back not knowing who it belongs to.
Walk the order: forget keys, clear the marker, rebuild the empty allowlist, enable new connections, show it on the LEDs.

## Slide 17: One more bug worth knowing about
Pathfinder Advanced - Op Program 12 | Lesson 3
16
Endianness, and an afternoon you will not get back
btaddr is a uint8_t[6], already in PRINTED order. Byte 0 prints first.
Op 11.2 printed it by counting DOWN from byte 5 to byte 0. So the address it showed you was the reverse of the real one.
The symptom: you write down the address it printed, paste it into another program, and nothing ever connects. Everything looks correct. The address is simply backwards.
Notes: This is the most human bug in the course. Everything looks correct and the address is simply backwards.
Describe the symptom before the cause: you write down what it printed, paste it somewhere else, and nothing ever connects.
The first lesson is a debugging habit: print it at both ends and compare character by character.
The second is a real category. Byte order is why network protocols specify it and why the word big-endian exists.
Op 12 now prints most significant byte first, matching every Bluetooth scanner they will ever use.

## Slide 18: One more bug worth knowing about (continued)
Pathfinder Advanced - Op Program 12 | Lesson 3
17
Two lessons:
  When an address will not work, print it at BOTH ends and compare them character by character.
  Byte order is a real category of bug. It is why network protocols specify it explicitly, and why the phrase big-endian exists.
KEY POINT Op 12 prints most significant byte first, which matches every Bluetooth scanner you will compare against.
Notes: (Continued from the previous slide - the same notes apply.)
This is the most human bug in the course. Everything looks correct and the address is simply backwards.
Describe the symptom before the cause: you write down what it printed, paste it somewhere else, and nothing ever connects.
The first lesson is a debugging habit: print it at both ends and compare character by character.
The second is a real category. Byte order is why network protocols specify it and why the word big-endian exists.
Op 12 now prints most significant byte first, matching every Bluetooth scanner they will ever use.

## Slide 19: Check yourself
Pathfinder Advanced - Op Program 12 | Lesson 3
18
Next lesson: never block, and never redraw for nothing.
1. What is a callback, and who calls it?
2. Why must the allowlist calls come after BP32.setup()?
3. Why rebuild the allowlist every boot instead of adding to it?
4. Why does Op 12 leave new Bluetooth connections enabled?
5. What actually happens when you call EEPROM.put()? When does the flash get written?
6. Why must you never call EEPROM.commit() from loop()?
7. What is the magic byte for, and why is it not sufficient on its own?
8. A vehicle refuses its own controller after a power cycle. Give two possible causes.
Notes: Conversation, not a test.
Answers: a callback is a function you supply and the library calls; the allowlist needs the stack up first, which is what BP32.setup() does; rebuilding keeps the sketch as the single source of truth.
New connections stay enabled so a vehicle can be re-paired without a recompile.
put() only writes the RAM copy; the flash is written by commit(). Never from loop, because flash wears out.
The magic byte says the data is ours, not that it is still valid for this version.
For question 8: the allowlist was applied before setup, or the paired address was never committed to EEPROM.