## Slide 1
LESSON 1
Architecture and Toolchain
How a real embedded program is put together: tabs, headers, capability flags, and a console you can talk to.
PORPOISE ROBOTICS - Precision Oceanographic Program On and In the Sea Environment
porpoiserobotics.org
Kevin Bowen, President - kbowen6@icloud.com
Malcom Graham, VP Education Louis Parker, VP Technology
Valen Farre, System Engineer Gary Howland, Animation
Eddie Revollo, Artificial Intelligence
Interns: Oscar Canazales, Krishnansh Vemulapalli, Soham Gangal, Erik Olsen
Three hours. Assumes you have driven a Pathfinder before.
Porpoise Robotics - proprietary. For use with Porpoise Robotics lessons.
Notes: Check the room: everybody here should have driven a Pathfinder and be comfortable reading C++. If somebody is not, pair them up now.
Have Op Program 12 open on the projector before you start. They will be looking at it all day.
Set expectations in the first minute: no new features. This is about how the program is built.

## Slide 2: What you will be able to do by the end
Pathfinder Advanced - Op Program 12 | Lesson 1
2
By the end of this lesson you will be able to:
1. Explain how the Arduino IDE assembles a multi-tab sketch, and why a type has to live in a header
2. Split a program by subsystem without breaking it
3. Say why the program detects its hardware rather than being told about it
4. Write a serial console that does not block the vehicle
5. Read the boot sequence of Op Program 12 and justify its order
Notes: Objective one is the one that will bite in the activity. The others are conceptual and get earned across the lesson.

## Slide 3: Who this course is for, and what it is not
Pathfinder Advanced - Op Program 12 | Lesson 1
3
You have driven a Pathfinder. You can read C++: functions, loops, structs, pointers, and you are not frightened of a header file.
This course is NOT more features. The vehicle does the same things it did on the beginner programs.
It is about how the program is BUILT: how you split 1300 lines so that somebody else can find things in it, how you make animations that never block the motors, how you store settings that survive a power cycle, and how you make a machine test its own hardware.
Along the way you will meet six real bugs from the previous version and see exactly why each one was wrong.
KEY POINT Every idea here transfers. None of it is specific to robots - it is how embedded software is written everywhere.
Notes: Be blunt about what this course is not. Some people arrive expecting more capability and are disappointed until you reframe it.
The six real bugs are the hook. Real code, real mistakes, and the reasons each one was wrong.
The note matters: none of this is robot-specific. It is how embedded software is written everywhere, and that is why it is worth three hours.

## Slide 4: Where this course goes
Pathfinder Advanced - Op Program 12 | Lesson 1
4
Lesson | Subject | The idea underneath it
1 | Architecture and the toolchain | Separate subsystems, and a way to talk to them
2 | Motors, resolution and ramping | Control quality, and integer math that lies
3 | Bluetooth and persistent storage | Identity that survives a power cycle
4 | The lighting state machine | Never block, and never redraw for nothing
5 | Sensors, self-test, diagnostics | A machine that can check itself
Notes: The right-hand column is the point. Each lesson has one transferable idea underneath the vehicle-specific detail.

## Slide 5: Today, in order
Pathfinder Advanced - Op Program 12 | Lesson 1
5
Time | What we do
0:00 | What changed from Op 11.2, and why
0:30 | One binary, two vehicles: capability flags
0:50 | How Arduino tabs really work, and why Config.h is a header
1:15 | BREAK (10 minutes)
1:25 | Upload a1a_tabs_and_config. Break it on purpose
1:55 | A serial console: reading without blocking, and parsing
2:15 | BREAK (10 minutes)
2:25 | Upload a1b_serial_console
2:45 | The boot sequence of Op Program 12, line by line
Notes: Two breaks. The tabs activity at 1:25 is the one that overruns - it is worth the time, so take it out of the boot-sequence walkthrough if you have to.

## Slide 6: Op Program 11.2 to 12 - what changed
Pathfinder Advanced - Op Program 12 | Lesson 1
6
Change | Why
FastLED replaced with Adafruit NeoPixel | FastLED 3.10.5 auto-enables an ESP-DSP FFT backend that does not build against the bluepad32 4.1.0 SDK. 11.2 stopped compiling.
Servo travel corrected to 1.0 - 2.0 ms | 11.2 used 0.5 - 2.5 ms, which can drive a servo into its end stops.
Paired address saved to EEPROM | 11.2 only added to the allowlist at runtime, so a reboot could leave a vehicle refusing its own controller.
Addresses print most significant byte first | 11.2 printed them backwards, so the address it told you to use was the reverse of the real one.
Speed ramping always reaches its target | Integer truncation stalled the old ramp one count short, forever.
Self-test compares against the measured baseline | 11.2 measured a baseline, printed it, then used fixed absolutes.
Standby lighting redrawn only when it changes | 11.2 pushed 32 LEDs on every pass of loop().
One 1292-line file split into eight | So that "where does pairing happen" has a one-word answer.
KEY POINT Read that list again at the end of the course. Most of them are mistakes that are easy to make and hard to see.
Notes: This is a real change log from a real project. Treat it as a case study, not a list.
The FastLED row is worth dwelling on: a library minor version broke the build through a dependency nobody chose. That happens constantly in the field.
The servo travel row is a safety bug - 0.5 to 2.5 ms can drive a servo into its end stops and cook it.
The address-printing bug is the cruellest kind: the program told you the wrong answer confidently.
Ask which of these they would have caught in review. Most people say the servo one and miss the integer truncation.

## Slide 7: One binary, two vehicles
Pathfinder Advanced - Op Program 12 | Lesson 1
7
The problem
Gen 2 vehicles have no current sensor. Gen 3 vehicles do.
Two separate builds means two things to keep in step, and somebody eventually flashes the wrong one.
The answer: DETECT the hardware at boot, and switch behavior on what is actually there.
How Op 12 does it
  Wire.begin(SDA, SCL);
  if (is_ina219_present()) {
  capabilities = CAP_SELF_TEST | CAP_CURRENT_MON;
  } else {
  capabilities = 0;
  }
Bit FLAGS, not booleans, so one byte carries several independent capabilities and a test is a single &.
Every feature that needs the sensor checks its flag first, and is a no-op without it.
KEY POINT Detect what is there rather than being told what is there. A configuration that can disagree with the hardware eventually will.
Notes: Two vehicles, one binary. Set the problem up before showing the solution.
Two separate builds is the obvious answer and the wrong one. Ask why - somebody eventually flashes the wrong image.
Detect what is there rather than being told what is there. That sentence is the transferable idea.
Bit flags rather than booleans: one byte carries several independent capabilities and a test is a single & operation. Show the arithmetic if anybody is shaky on bitwise operators.

## Slide 8
Pathfinder Advanced - Op Program 12 | Lesson 1
8
Tabs and Config.h
About 55 minutes
Architecture
done
Tabs and Config.h
NOW
The console
Notes: Twenty seconds. First activity.

## Slide 9: How Arduino tabs actually work
Pathfinder Advanced - Op Program 12 | Lesson 1
9
Convenient, and exactly one trap
Every .ino file in the sketch folder is a tab in the IDE.
Before compiling, the IDE CONCATENATES them into one file - the one named after the folder first, then the rest alphabetically - and generates prototypes at the top.
Two consequences you have to know:
  Functions and globals cross tabs with NO header needed. Lighting.ino can call strip and read NUM_LEDS with no include.
  TYPES do not. The generated prototypes go ABOVE your code, so a prototype mentioning an enum or struct you declared in a tab will not compile - the type is not defined yet.
That is precisely why Config.h is a real header rather than a ninth tab. It is #included by the main sketch, so it is defined before the prototypes appear.
KEY POINT Op 12's Config.h opens with a paragraph saying this. Now you know what it is warning you about.
Notes: This is the slide the activity is built on. Go slowly.
The IDE concatenates the tabs and generates prototypes ABOVE your code. Draw that on the board - the ordering is the whole explanation.
Functions and globals cross tabs freely. Types do not, because the generated prototype mentions a type that is not defined yet at that point.
That is precisely why Config.h is a real header. Not style - necessity.

## Slide 10: The eight files, and what each one owns
Pathfinder Advanced - Op Program 12 | Lesson 1
10
One subsystem per file. The rule that makes it work: each tab owns its own state, and other tabs go through its functions.
File | Owns
Pathfinder_Op_Program12.ino | setup(), loop(), the hardware objects, the shared state
Config.h | Every tunable number and every custom type
Motors.ino | PWM setup, drive modes, ramping, servos, throttle modes
Lighting.ino | Color helpers, every animation, the lighting state machine
Bluetooth.ino | Connection callbacks, the allowlist, the pairing workflow
Console.ino | The serial command interface, EEPROM settings, diagnostics
Sensors.ino | The INA219 driver
SelfTest.ino | The powered motor check
KEY POINT Nothing in the compiler enforces that. Every tab can see every global. It is a convention, and it is the only thing standing between you and 1292 lines again.
Notes: Eight files, one subsystem each. Read the table, then say the rule underneath it: each tab owns its own state and others go through its functions.
The note is the honest part: nothing in the compiler enforces this. Every tab can see every global. It is a convention held by discipline.
Ask what happens when somebody breaks the convention. The answer is that the program still compiles, which is exactly why it is dangerous.

## Slide 11: Do it now - three files, one program
Pathfinder Advanced - Op Program 12 | Lesson 1
11
UPLOAD AND RUN: a1a_tabs_and_config (30 minutes)
1. Open it. Look at the tab bar: the sketch, Config.h, Blinker.ino.
2. Upload it. It blinks and reports, and swaps speed every 5 s.
3. Change BLINK_SLOW_MS in Config.h. Notice you touched neither .ino file.
4. Add a fourth file, Reporter.ino, with a function in it. Call it from loop(). Notice you declared it nowhere.
5. Now MOVE the BlinkMode enum out of Config.h and into Blinker.ino. Compile. READ THE ERROR CAREFULLY.
6. Put it back.
What you should see
Step 5 fails with an error about BlinkMode not naming a type, pointing at a line you did not write.
Answer these
Whose line is the error actually on?
Why does moving a FUNCTION between tabs work fine, but moving a TYPE does not?
Notes: Step 5 is the whole point of this activity. Do not warn them what the error will look like.
The error points at a line they did not write, in generated code. That experience is worth more than the explanation on the previous slide.
Answer to the first question: the error is on a generated prototype line, not on any line in their file.
Answer to the second: functions are only NAMED in the prototype, but a type has to be DEFINED before the prototype that mentions it.
Thirty minutes, and it is worth every one of them.

## Slide 12
Pathfinder Advanced - Op Program 12 | Lesson 1
12
The console
About 40 minutes
Architecture
done
Tabs and Config.h
done
The console
NOW
Notes: Twenty seconds. Second activity.

## Slide 13: Why a console changes what a vehicle is
Pathfinder Advanced - Op Program 12 | Lesson 1
13
From opaque binary to something you can ask questions
A compiled binary is opaque. You can see what it does, not what it thinks.
A serial console turns it into something you can interrogate:
  help what can this thing do
  diag what does it think is happening right now
  pair change its behavior without a laptop full of toolchains
  dynamics retune the deadzones between races
The practical difference: at a track event, tuning a vehicle stops being an edit-compile-upload cycle and becomes a conversation. On Op 12 those settings then go to EEPROM, so the tuning survives.
This is not a toy idea. Industrial controllers, network switches and flight computers all have one, for exactly this reason.
Notes: A compiled binary is opaque. You can see what it does, not what it thinks. That is the framing.
The four commands on the slide are the four things people actually want at a track event.
Tuning stops being an edit-compile-upload cycle and becomes a conversation. That is a real productivity difference, not a nicety.
Industrial controllers, network switches and flight computers all have one. This is standard practice, not a toy.

## Slide 14: Reading a line without stopping the vehicle
Pathfinder Advanced - Op Program 12 | Lesson 1
14
a1b_serial_console.ino
void handleSerial() {
while (Serial.available() > 0) {
char c = (char)Serial.read();
if (c == '\n' || c == '\r') { // accept both
if (input_line.length() > 0) {
runCommand(input_line);
input_line = "";
}
continue;
}
if (c >= 32 && c < 127 && input_line.length() < 80) {
input_line += c;
}
}
}
Serial.readStringUntil() would WAIT for a newline. While it waits the vehicle is not driving. Never use it on a moving machine.
This takes whatever bytes have arrived and returns immediately, every time.
The Serial Monitor sends whatever its line-ending dropdown says: nothing, LF, CR, or both. Handle all four or the console looks broken to whoever set theirs differently.
The length cap matters. Without it a stuck sender grows the String until the ESP32 runs out of heap.
Notes: Serial.readStringUntil() WAITS. On a moving vehicle that is unacceptable. Say it plainly.
This version takes whatever bytes have arrived and returns immediately, every time. That is the non-blocking pattern from beginner Lesson 5, applied to input.
The line-ending handling looks like paranoia until you watch a console appear broken because the Serial Monitor dropdown was set differently.
The printable-character and length checks are the input validation. Worth pointing out that they are not optional.

## Slide 15: Do it now - a console
Pathfinder Advanced - Op Program 12 | Lesson 1
15
UPLOAD AND RUN: a1b_serial_console (25 minutes)
1. Upload it, open the Serial Monitor, type help.
2. Try every command. Then type something that is not a command.
3. Type set rate abc. What happens? Why does the range check catch it?
4. Change your Serial Monitor line-ending setting to each of its four options. Does the console still work in all four?
5. Add a command of your own: toggle, that flips a bool.
6. Open Console.ino in Op Program 12 and find the same three problems being solved there.
What you should see
A prompt, echoed typing, working backspace, and commands that run while the LED keeps blinking on its own schedule.
Answer these
toInt() returns 0 for anything it cannot parse. Why does that make range checking essential rather than optional?
Notes: Step 4 is the one people skip. Make them try all four line-ending settings - it is the fastest way to appreciate the previous slide.
Step 5 is the first thing they write themselves today.
Step 6 sends them into the real program to find the same three problems solved there. That is the bridge to the rest of the course.
The answer to the question: toInt() returns 0 for anything unparseable, so a typo silently becomes a valid-looking zero. Range checking is what catches it.

## Slide 16: The boot sequence of Op Program 12
Pathfinder Advanced - Op Program 12 | Lesson 1
16
Pathfinder_Op_Program12.ino
void setup() {
Serial.begin(115200);
EEPROM.begin(EEPROM_SIZE);
loadSettings(); // tuning, range checked
Wire.begin(I2C_SDA_PIN, I2C_SCL_PIN);
if (is_ina219_present()) { // which vehicle am I?
vehicle_config.capabilities = CAP_SELF_TEST | CAP_CURRENT_MON;
ina219_init();
} else {
vehicle_config.capabilities = 0;
test_state = TEST_DISABLED;
}
The ORDER is deliberate.
Settings first, because everything else may depend on them.
Hardware detection next, because it decides what the rest of setup is even allowed to do.
Motors before anything slow. An uninitialised H-bridge pin floats, and a floating pin can twitch a motor. Get the outputs into a known safe state as early as you can.
Radio last. It is the slowest thing to come up and nothing else waits on it.
Notes: The order is the lesson, not the code. Walk down it and ask why each step is where it is.
Settings first, because everything after may depend on them. Then detect the hardware, because behavior branches on it.
Motors before lights, because getting the outputs into a safe state matters more than anything pretty.
Radio last, because a controller connecting to a half-initialised vehicle is the worst possible moment.
Ask them to justify a different order. Making them defend it is better than telling them.

## Slide 17: The boot sequence of Op Program 12 (continued)
Pathfinder Advanced - Op Program 12 | Lesson 1
17
Pathfinder_Op_Program12.ino
setup_motors(); // outputs safe FIRST
setup_servos();
strip.begin(); // then the lights
set_disconnected_lighting();
setup_bluetooth(); // then the radio
pinMode(PAIR_TRIGGER_PIN, INPUT_PULLUP);
pinMode(TEST_PIN, INPUT);
}
Notes: (Continued from the previous slide - the same notes apply.)
The order is the lesson, not the code. Walk down it and ask why each step is where it is.
Settings first, because everything after may depend on them. Then detect the hardware, because behavior branches on it.
Motors before lights, because getting the outputs into a safe state matters more than anything pretty.
Radio last, because a controller connecting to a half-initialised vehicle is the worst possible moment.
Ask them to justify a different order. Making them defend it is better than telling them.

## Slide 18: How a command gets from your thumb to a wheel
Pathfinder Advanced - Op Program 12 | Lesson 1
18
Bluetooth gamepad
you move a stick
Bluetooth
radio, 2.4 GHz
ESP32
your program runs here
DRV8871 drivers
4 motors
12 13 16 17 18 19 22 23
WS2812B strip
32 LEDs
GPIO 5
Servo headers
up to 4 servos
25 26 27 14
KEY POINT Everything the vehicle can do happens on one of those three outputs. The rest of the program is deciding what to send.
Notes: Walk it left to right with a real vehicle in your hand, touching each box as you name it.
The point of the diagram is that nothing here is magic - every arrow is a wire or a radio link you can point at.
Ask where THEIR program sits. The answer is the ESP32 box, and everything either side of it is fixed hardware they inherit.
Come back to this slide whenever somebody is stuck: naming which box the fault is in is most of the debugging.

## Slide 19: The hardware this program is talking to
Pathfinder Advanced - Op Program 12 | Lesson 1
19
Nothing here is new to you. What is new is that one binary has to cope with two different versions of it.
Part | Where | What Op 12 does with it
ESP32 DevKitC, 38 pin | - | 240 MHz dual core, Bluetooth, 16 PWM channels
4 x DRV8871 H-bridge | 12/13, 18/19, 22/23, 16/17 | 10-bit PWM at 30 kHz, hybrid drive
32 x WS2812B | GPIO 5 | One loop: 0-15 front, 16-31 rear
4 x servo header | 25, 26, 27, 14 | 50 Hz, 1.0 to 2.0 ms, one per stick direction
INA219 current sensor | I2C on 32 / 33 | Gen 3 only. Detected at boot.
BOOT button | GPIO 0 | Held low to enter pairing mode
Self-test jumper | GPIO 34 | Input-only pin, external pull-down
4S LiPo, 3300 mAh | - | About 16 V charged
WATCH OUT GPIO 34-39 are INPUT ONLY on the ESP32 and have no internal pull resistors. That is why the self-test pin needs one on the board.
Notes: This is reference, not teaching. Point at it and move on.
The note is the one thing to say out loud: GPIO 34 to 39 are input only and have no internal pull-up, which is why the self-test jumper needs an external pull-down.
Worth printing for the rest of the course.

## Slide 20: Reading a program you did not write
Pathfinder Advanced - Op Program 12 | Lesson 1
20
Header, then Config.h, then setup(), then loop()
You are about to be handed 1300 lines across eight files. Front to back is the slowest possible way in. A better order:
  1. The header comment: the hardware, the controls, and in this case the change log.
  2. Config.h. Every number the program cares about, in one place. What it lets you tune tells you what it can do.
  3. setup(). What has to be true before anything runs.
  4. loop(). The whole shape, in one screen.
  5. Only then, the subsystem that interests you.
Vocabulary first, then skeleton, then detail. The other way round means reading Lighting.ino with no idea what led_mode is or who sets it.
EXERCISE, ten minutes. Read Op 12 in that order and write down three questions. We will answer them over the next four lessons.
Notes: This is the most useful slide in the lesson for anybody who will read somebody else's code again - which is all of them.
Vocabulary first, then skeleton, then detail. Say why: reading Lighting.ino with no idea what led_mode is or who sets it is wasted time.
Run the ten-minute exercise properly. Time it, and get answers from three different groups.
Point out that Config.h tells you what the program can DO, because it tells you what somebody thought was worth tuning.

## Slide 21: Check yourself
Pathfinder Advanced - Op Program 12 | Lesson 1
21
Next lesson: motors, and integer math that quietly lies to you.
1. Why is Config.h a header file rather than a ninth tab?
2. In what order does the Arduino IDE concatenate your tabs?
3. Why does Op 12 detect the current sensor rather than being told which generation it is running on?
4. Why are capabilities bit flags rather than separate booleans?
5. Name two things wrong with Serial.readStringUntil() on a moving vehicle.
6. Why does setup() initialise the motors before the LEDs?
7. Every tab can see every global. Why is that both the convenience and the danger?
Notes: Conversation, not a test.
Answers: Config.h is a header because generated prototypes sit above the code and a type must already be defined; tabs concatenate with the folder-named file first and the rest alphabetically; detection avoids a configuration that can disagree with reality.
Bit flags let one byte carry several independent capabilities and make a test a single & operation.
readStringUntil blocks, and it also depends on a timeout you did not choose.
Motors before LEDs so the outputs are safe before anything else happens.
The last question has no clean answer, and that is the point - shared globals are convenient exactly because nothing stops you.