## Slide 1
LESSON 3
Controller Programming
Bluetooth, thumbsticks, deadzones, and turning a number from your thumb into a speed for four wheels.
PORPOISE ROBOTICS - Precision Oceanographic Program On and In the Sea Environment
porpoiserobotics.org
Kevin Bowen, President - kbowen6@icloud.com
Malcom Graham, VP Education Louis Parker, VP Technology
Valen Farre, System Engineer Gary Howland, Animation
Eddie Revollo, Artificial Intelligence
Interns: Oscar Canazales, Krishnansh Vemulapalli, Soham Gangal, Erik Olsen
Three hours. Bring the PS3 controller paired to your vehicle.
Porpoise Robotics - proprietary. For use with Porpoise Robotics lessons.
Notes: Controllers charged and paired before the class starts. A flat pad costs you twenty minutes you do not have.
Today is the lesson they came for. Say so, then make them earn it - everything before the last hour is print-only.

## Slide 2: What you will be able to do by the end
Pathfinder Beginner - PS3 | Lesson 3
2
By the end of this lesson you will be able to:
1. Explain how a controller reaches one vehicle and not another
2. Say what a deadzone is for, and what goes wrong without one
3. Use map() to turn a stick reading into a motor speed
4. Mix a forward value and a turn value into two wheel speeds
5. Drive the vehicle under your own control
6. Write the failsafe that stops the motors when the controller drops
Notes: Objective six, the failsafe, is the one that matters beyond this course. Flag it now and come back to it at the end.

## Slide 3: Where we got to last lesson
Pathfinder Beginner - PS3 | Lesson 3
3
You know how an H-bridge reverses a motor, and how PWM sets its speed.
You watched duty and speed change together on the Serial Monitor.
You drove a square you calculated, and found out why it did not close.
Today you take the wheel.
KEY POINT Everything today until the last hour is print-only. Nothing moves until you have seen the numbers first.
Notes: Sixty seconds, then straight on.
The note is the discipline for the day: see the numbers first, drive second. It stops a room full of vehicles bolting during the first upload.

## Slide 4: Today, in order
Pathfinder Beginner - PS3 | Lesson 3
4
Time | What we do
0:00 | Recap. What Bluetooth is, and how a pad finds a vehicle
0:25 | One vehicle, one controller
0:50 | Upload l3a_controller_check. Find every button and axis
1:15 | BREAK (10 minutes)
1:25 | The deadzone problem, and map()
1:50 | Upload l3b_deadzone_and_map. Watch the arithmetic
2:10 | BREAK (10 minutes)
2:20 | Mixing forward and turn
2:35 | Upload l3c_tank_drive. Drive it
2:55 | Failsafe, and what happens when the link drops
Notes: Point out that the vehicle does not move until 2:35. Manage the disappointment early rather than fighting it all lesson.

## Slide 5: What Bluetooth is doing
Pathfinder Beginner - PS3 | Lesson 3
5
A radio link, and a phone number for each device
A short-range radio link in the 2.4 GHz band - the same band as Wi-Fi, microwave ovens and almost everything else.
It hops between 79 narrow channels many times a second, so a busy band does not stop it. That is why twenty vehicles in one room actually works.
Range is tens of meters, and it goes down sharply if somebody stands between the pad and the vehicle.
Every Bluetooth device has an ADDRESS - six bytes, written as six pairs of hexadecimal digits, like 02:02:03:04:05:08. It is the equivalent of a phone number.
The ESP32 has Bluetooth built into the chip. That is a large part of why we use it.
KEY POINT A Bluetooth sketch fills about 85% of the ESP32's program storage. That is the radio stack, not your code - but it does mean there is not much room left, so keep additions lean.
Notes: Keep the radio theory to two minutes. The one thing that must land is that every device has an address, and an address is like a phone number.
The channel-hopping detail answers the question they are about to ask: why twenty vehicles in one room actually works.
The 85% storage note is worth mentioning. It explains why a Bluetooth sketch takes so long to upload and why some boards run out of room.

## Slide 6: One vehicle, one controller - read the sticker
Pathfinder Beginner - PS3 | Lesson 3
6
A PS3 controller has no discovery mode. It talks to ONE Bluetooth address and no other - we program and label every pad before the lesson.
The number on your pad's sticker is the end of that address:
  02:02:03:04:05:NN NN = the number on the sticker
YOU put it into every program that uses the controller, near the top:
  const char *PS3_MAC_ADDRESS = "02:02:03:04:05:00";
Change the 00 to your number. Left at 00, nothing connects - so a forgotten edit can never drive somebody else's vehicle.
Pad will not connect? Check the number in the sketch against the sticker before anything else.
WATCH OUT Every program that uses the controller has a CHANGE THIS BEFORE YOU UPLOAD block. Look for it before every upload.
Notes: Kevin's instruction, 2026-09-05: we program and label the controllers, so students never run SixaxisPairTool. What they DO have to do is copy the sticker number into each program they upload: l3a, l3b, l3c, l5b, l5c and pathfinder_ps3.
Say the odd part plainly: on a PS3 pad it is the CONTROLLER that is told which address to talk to. The sketch makes the ESP32 answer to that address.
Why every sketch ships ending in 00: with a real address as the default, a student who forgot to change it would drive whichever vehicle owns that pad. Now forgetting means nothing connects, and the Serial Monitor prints the address the sketch is listening as.
FOR YOU, NOT FOR THE SLIDE - how the labelling is done. Plug the pad into a Windows PC over USB, open SixaxisPairTool, type 02:02:03:04:05:NN and click Update, then put NN on a sticker on the pad.
Also for you: keep the first pair of digits EVEN - 02 is what we use. An odd one is not an ordinary device address and failed silently with the original library, which is a very confusing way to spend an afternoon.
Check the stickers around the room now, before anybody uploads. Every term somebody loses a morning to a pad that was picked up off the wrong table.

## Slide 7: The PS3 controller - every name you will need
Pathfinder Beginner - PS3 | Lesson 3
7
Notes: This is a reference page and it is deliberately nothing but the picture. Leave it up while they work.
Hold a real controller alongside it and name the parts. Two analog sticks, a D-pad, four face buttons, four shoulder buttons, two triggers, and three in the middle.
Every one of those has a name in the program, and they are about to press all of them and see what each is called.
Tell them to photograph this slide. They will want it again in Lessons 4 and 5.

## Slide 8: How the ESP32 controls the motors
Pathfinder Beginner - PS3 | Lesson 3
8
YOUR PROGRAM
H-BRIDGE DRIVER
MOTOR
ledcWrite -> GPIO 12 / 13
DRV8871
Front left wheel
ledcWrite -> GPIO 18 / 19
DRV8871
Rear left wheel
ledcWrite -> GPIO 22 / 23
DRV8871
Front right wheel
ledcWrite -> GPIO 16 / 17
DRV8871
Rear right wheel
KEY POINT TWO pins per motor, and the driver is what makes it possible. An ESP32 pin gives you 3.3 volts and about 20 milliamps; a motor wants battery voltage and amps. The DRV8871 takes the small signal and switches the big one.
Notes: Read one row left to right and the whole thing is obvious: two pins, a driver chip, a motor.
The driver is the part worth naming. The ESP32 pin can supply about 20 milliamps at 3.3 volts. A motor wants amps at battery voltage. The DRV8871 is what stands between them.
Two pins per motor, not one. Which of the two you drive is what decides the direction - that is the H-bridge from Lesson 2.
Point out that the pin numbers on this slide are read out of the sketch when the deck is built, so if they look at the file they will find the same ones.
Worth pausing on the fact that all four rows are identical. Four motors is not four times the thinking - it is the same thinking, four times.

## Slide 9: Two kinds of control, and the axes they move
Pathfinder Beginner - PS3 | Lesson 3
9
Digital: pressed or not
A digital reading is true or false, with nothing in between.
The D-pad, Select, Start and the PS button, and clicking either stick in.
Good for: on/off, mode changes, one-shot actions.
On this track:
  Ps3.data.button.square
Analog: how far
An analog reading says HOW FAR, not just whether.
Both thumbsticks, on two axes each, reading -128 to +127.
The TRIGGERS are analog too, and so are the shoulder and face buttons - a Sixaxis reports how hard you press.
Good for: speed, steering, aiming a servo.
  Ps3.data.analog.stick.lx // left/right
  Ps3.data.analog.stick.ly // up/down
WATCH OUT Push a stick UP and the number goes NEGATIVE. That catches everybody. It is why the driving code has a minus sign in front of the Y reading.
Notes: Digital and analog is a distinction they will use for the rest of their lives. Two minutes, properly.
Kevin caught this in the 2026-09-05 review: the PS3 triggers are ANALOG, not digital. So are the shoulder and face buttons - a Sixaxis reports pressure on all of them. Almost every program reads them as digital anyway, which is why it is easy to get wrong.
A press can read differently from a light one, and you can still treat any of them as a plain yes or no - which is mostly what we do, and why it is easy to get wrong.
If you have five spare minutes, have them squeeze a trigger slowly in l3a_controller_check and watch the number climb.
The warning panel is the one to read out. Push a stick up and the number goes negative - it catches everybody, and it is why there is a minus sign in the driving code.
Have a controller in your hand and press the things as you name them.

## Slide 10: Six degrees of freedom
Pathfinder Beginner - PS3 | Lesson 3
10
Any rigid object in space can move in six independent ways. Three are translations - sliding along an axis - and three are rotations.
TRANSLATION
  Forward and back - surge
  Side to side - sway
  Up and down - heave
ROTATION
  Roll - tipping left or right about the fore-aft axis
  Pitch - nose up or nose down
  Yaw - turning left or right, which is your steering
A ground vehicle on a flat floor really only controls surge and yaw. A submersible or an aircraft controls all six, which is why they need far more from the operator.
KEY POINT The PS3 controller was originally called the Sixaxis because it could sense all six. Spelled backwards, Sixaxis is still Sixaxis.
Notes: Six degrees of freedom is genuinely useful vocabulary and it costs three minutes.
Demonstrate with your hand: three slides, three twists.
A rover on a flat floor really only has surge and yaw. That is why one stick is enough here and why a submersible pilot needs two.
The Sixaxis palindrome is a cheap laugh and it makes the name stick.

## Slide 11: Six degrees of freedom, and the two your rover has
Pathfinder Beginner - PS3 | Lesson 3
11
TRANSLATION - sliding along an axis
ROTATION - turning about an axis
SURGE
forward and back
X axis
your rover controls this one
SWAY
left and right
Y axis
HEAVE
up and down
Z axis
ROLL
tipping left or right
about X
PITCH
nose up or nose down
about Y
YAW
turning left or right
about Z
your rover controls this one
LEFT STICK on the PS3 controller -> surge and yaw
RIGHT STICK -> the four servos
KEY POINT A rover controls two of the six, so one stick drives it and the other is free to aim servos. A submersible controls all six, and an ROV pilot needs both sticks to fly it.
Notes: Six ways a rigid body can move. Three slides, three twists, and nothing else.
Demonstrate with your hand held flat before you show the diagram. Slide it forward, sideways, up. Then tip it, nose it down, spin it.
The two boxed in teal are the two a rover on a flat floor can actually control. That is why one stick with two axes is enough here.
A submersible or an aircraft controls all six, which is why an ROV pilot needs two sticks and far more practice.
Sway is the interesting one to ask about. A rover cannot slide sideways - it has to yaw and then surge. Ask them why.

## Slide 12
Pathfinder Beginner - PS3 | Lesson 3
12
What the pad sends
About 25 minutes
Bluetooth and pairing
done
What the pad sends
NOW
Deadzone and map
Driving it
Notes: Twenty seconds. First of three.

## Slide 13: Do it now - what does the controller actually send?
Pathfinder Beginner - PS3 | Lesson 3
13
UPLOAD AND RUN: l3a_controller_check (25 minutes)
1. Set PS3_MAC_ADDRESS to the number on your controller's sticker. Upload, and open the Serial Monitor.
2. Press the PS button on the controller.
3. Press every button in turn and match it to the printed name.
4. Push the left stick fully UP. Positive or negative?
5. Let go of the sticks and DO NOT touch the controller. Does it print exactly 0, or does it drift?
6. Push a stick diagonally. Watch x and y move together.
7. Squeeze L2 slowly. It is not just on or off - watch the number.
What you should see
A line for every press and every release, and up to four lines a second while a stick moves.
Answer these
Which way is negative on the Y axis?
How far does your stick drift when nobody is touching it?
Notes: This is a reading exercise, not a driving one. Nothing moves.
Step 5 is the one that sets up the whole deadzone section: hands off, and watch the number refuse to sit at zero.
Step 1 is the first time they set the address, and they will do it again in every controller program from here on. The sketch prints which address it is listening as. If that still ends in 00, that is why nothing connects.
Walk round with a list of button names. Somebody will find a button that prints nothing, and that is usually a third-party pad rather than a fault.
The sticks print at most four times a second, on purpose - PRINT_MS in the sketch. Anybody who wants to see why can set it to 20 and watch the window scroll away.
ANSWER, Y axis: pushing UP gives a NEGATIVE number, down a positive one (-128 to +127). That is why the driving code puts a minus sign in front of the Y reading.
ANSWER, drift: it depends on the pad, which is the point. A worn stick usually rests a few counts off zero. Collect the numbers from the room - the biggest one is what the deadzone has to beat, and it is the next section.

## Slide 14
Pathfinder Beginner - PS3 | Lesson 3
14
Deadzone and map
About 45 minutes
Bluetooth and pairing
done
What the pad sends
done
Deadzone and map
NOW
Driving it
Notes: Twenty seconds. Two of three.

## Slide 15: The problem with believing the stick
Pathfinder Beginner - PS3 | Lesson 3
15
Deadzone
A thumbstick that has been thumbed by a hundred students does not come back to exactly zero.
You just measured it. Yours probably reads a few counts either side of center when nobody is touching it.
If we fed that straight to the motors, the vehicle would creep across the room on its own while the controller sat on the desk. In a classroom with twenty vehicles, that is not a minor annoyance.
The answer is a DEADZONE: any reading smaller than a threshold is treated as a firm, deliberate zero.
On this track the deadzone is 20, which is about 16% of the stick travel.
Too small and the vehicle creeps. Too big and you waste the stick.
Notes: They measured the drift ten minutes ago. Ask for numbers before you explain anything.
Paint the picture: twenty vehicles creeping across a classroom floor with nobody touching a controller.
The deadzone value and percentage on this slide are read out of the sketch at build time, so they match the file they are about to edit.
The trade-off is the point: too small and it creeps, too big and you waste the stick. They will feel both in the next activity.

## Slide 16: From thumbstick to motor speed
Pathfinder Beginner - PS3 | Lesson 3
16
stick reading 0 to 127
motor
speed
0 to 255
DEADZONE answer is 0
map() stretches what is left across the whole speed range
20
stickToSpeed()
if (abs(v) < DEADZONE)
return 0;
size = map(abs(v),
DEADZONE, 127,
MOTOR_MIN, maxSpeed);
return (v > 0) ? size
: -size;
Why a deadzone at all?
A worn stick does not return
to exactly zero. Without this
the vehicle creeps away on
its own.
Notes: The two numbers that matter are the deadzone and the top of the stick range. Everything else on the slide follows from those.
Ask why the ramp does not start at the origin. The answer - a stick at rest is never exactly centered - is worth getting from the room rather than telling them.
With MOTOR_MIN at 0 the ramp leaves the deadzone edge at zero speed, with no jump. Step 5 of the next activity sets MOTOR_MIN to 60, and then the speed jumps from 0 straight to 60 at the edge. That is what a speed floor looks like.
Come back to this diagram when somebody's vehicle creeps on its own.

## Slide 17: map() - the most useful function in the course
Pathfinder Beginner - PS3 | Lesson 3
17
the idea, and how the program uses it
map(value, fromLow, fromHigh, toLow, toHigh)
// "value sits somewhere between fromLow and fromHigh.
// Where does it sit between toLow and toHigh?"
map(0, 0, 127, 0, 255) -> 0
map(63, 0, 127, 0, 255) -> 126
map(127, 0, 127, 0, 255) -> 255
// In stickToSpeed the low end is the DEADZONE, not zero,
// so the leftover travel is stretched across the whole
// speed range. Without that you could never reach 255.
size = map(abs(v), 20, 127, MOTOR_MIN, maxSpeed);
map() is just proportion. Nothing more.
It works in WHOLE numbers. 63 x 255 / 127 is 126.496..., and the fraction is thrown away - not rounded - just like 7 / 2 in Lesson 1.
It does NOT clamp. Feed it something outside the input range and you get something outside the output range, which is why the program calls constrain() straight afterwards.
abs() throws away the sign, so we map the SIZE of the push and put the direction back at the end.
Notes: map() is just proportion. Say that first, then show the three worked examples.
Make them work the middle one out before you say it. Half the stick is NOT exactly half speed, because map() works in whole numbers and throws the fraction away - the 7 / 2 trap from Lesson 1, in a place where it actually matters.
The important subtlety is on the last line: the low end is the DEADZONE, not zero. Without that, the leftover travel could never reach full speed.
map() does not clamp. Feed it something outside the range and you get something outside the range - which is exactly why constrain() exists.
Get them to work out one example on paper before the activity.

## Slide 18: Do it now - watch the arithmetic
Pathfinder Beginner - PS3 | Lesson 3
18
UPLOAD AND RUN: l3b_deadzone_and_map (20 minutes)
1. Set PS3_MAC_ADDRESS to the number on your controller's sticker. Upload it. Nothing moves - this is print only.
2. Push the stick VERY slowly from center to full forward. Watch both columns. Where does the speed stop being 0?
3. Set STICK_DEADZONE to 0. Upload. Put the controller down and do not touch it. Does the speed stay at 0?
4. Set it to 101. How much of the stick is now wasted?
5. Put it back. Now set MOTOR_MIN to 60 and watch what happens the instant you leave the deadzone.
What you should see
Two columns: the raw number from the controller, and the motor speed it turns into. A new line only when the stick moves.
Answer these
With the deadzone at 0, what does the vehicle do when nobody is holding the controller?
What does MOTOR_MIN = 60 change, and when would you want it?
Notes: Print only. Nothing moves, so nobody needs a block.
Step 3 is the demonstration of the whole idea: deadzone at zero, hands off, and the numbers will not sit still.
Step 4 makes the opposite mistake on purpose. Ask them how much of the stick is left.
Step 5 previews MOTOR_MIN, which they met in Lesson 2. The jump the instant they leave the deadzone is what a raised minimum feels like.
ANSWER, deadzone 0: it would creep. The resting drift is no longer thrown away, so it turns into a small motor speed - the speed column stops reading 0 even with nobody touching the pad.
ANSWER, MOTOR_MIN = 60: the speed jumps from 0 straight to 60 the moment the stick leaves the deadzone, instead of starting from 0. You want it for motors that will not turn at all below some duty - the number they found with l2b_speed_ramp. These vehicles drive fine without it, which is why it ships at 0.

## Slide 19
Pathfinder Beginner - PS3 | Lesson 3
19
Driving it
About 35 minutes
Bluetooth and pairing
done
What the pad sends
done
Deadzone and map
done
Driving it
NOW
Notes: Twenty seconds, then clear the floor.

## Slide 20: Mixing, and why steering has its own limit
Pathfinder Beginner - PS3 | Lesson 3
20
Full speed forwards, 75% steering
left = forward + turn right = forward - turn
Driving gets the full MOTOR_MAX of 255.
Steering gets turnMax, which is 75% of that by default - 191.
Why? Because at full power a small nudge sideways spins the vehicle faster than anybody can correct for. Holding steering to 75% makes it controllable without making it slow.
The full program lets you switch between the two with L3 (click the left stick in). Sharp mode is for spinning on the spot deliberately; normal mode is for actually getting somewhere.
constrain() catches the overflow. forward 200 plus turn 60 is 260, which is more than a motor can take.
Notes: Two lines of arithmetic. Write them on the board and work an example with the room before you show the slide.
The 75% steering limit is a design decision, not a limitation. Explain the reasoning: full-power steering spins faster than anybody can correct for.
constrain() is what catches forward 200 plus turn 60. Ask what would happen without it - the number wraps past what the motor can take and the vehicle turns the wrong way.

## Slide 21: l3c_tank_drive - the whole of loop()
Pathfinder Beginner - PS3 | Lesson 3
21
l3c_tank_drive.ino
void loop() {
if (!Ps3.isConnected()) {
drive(0, 0); // never drive without a controller
return;
}
int leftStickX = Ps3.data.analog.stick.lx;
int leftStickY = Ps3.data.analog.stick.ly;
int forward = stickToSpeed(-leftStickY, MOTOR_MAX);
int turn = stickToSpeed(leftStickX, turnMax);
int leftSpeed = constrain(forward + turn, -MOTOR_MAX, MOTOR_MAX);
int rightSpeed = constrain(forward - turn, -MOTOR_MAX, MOTOR_MAX);
drive(leftSpeed, rightSpeed);
}
Read the first four lines again. If there is no controller, the motors stop and we go round again. That is the FAILSAFE, and it is the most important part of the program.
Note the minus sign on leftStickY. Up is negative.
Driving gets MOTOR_MAX; steering gets turnMax.
Everything else you have already seen.
Notes: Read the first four lines twice. That is the failsafe, and it is the most important thing in the file.
The minus sign in front of leftStickY is the up-is-negative fix from earlier. Point back at it.
Ask which line sets speed and which sets steering, then which one limits steering to 75%.
This is the first program in the course they could plausibly have written themselves. Say so.

## Slide 22: Do it now - drive it
Pathfinder Beginner - PS3 | Lesson 3
22
UPLOAD AND RUN: l3c_tank_drive (30 minutes)
1. Set PS3_MAC_ADDRESS to the number on your controller's sticker. Then wheels off the ground, upload, and check that up is forward and right is right BEFORE you put it down.
2. Put it on the floor in a clear space and drive.
What you should see
A vehicle that goes where you point it.
Answer these
What happened when the pad went out of range, and which four lines made that happen?
Notes: Step 1 is not optional. Wheels off the ground, check up is forward and right is right, every single upload.
Step 3 is the failsafe demonstration, and it needs setting up. Kevin caught this in the 2026-09-08 review: the slide used to say switch the pad off, and neither of these controllers CAN be switched off by hand. Walking out of range is the demonstration that actually works.
Send one person down the corridor with the pad while the rest of the group watches the wheels. Thirty feet, or one wall, is usually enough. If the room is small, power-cycle the vehicle instead and push the stick while it is disconnected - same guard, seen from the other side.
Steps 5 and 6 are deliberate breakages, and the line numbers on the slide are read out of the sketch when the deck is built, so they are right for the track in front of you.
Swapped signs give a vehicle that steers backwards. Dropping the turn term from the right side only gives something that swings wide one way and barely turns the other - the left wheels still get forward + turn while the right ones get forward alone.
Make them put both back before they leave.
Give this the full thirty minutes. It is the payoff for three lessons of groundwork.
ANSWER: the wheels stopped within about a second of the link dropping, and picked up again when the pad came back in range. The four lines are the if at the very top of loop(): no controller, so drive(0, 0) and return before anything else runs.

## Slide 23: Do it now - drive it (continued)
Pathfinder Beginner - PS3 | Lesson 3
23
UPLOAD AND RUN: l3c_tank_drive
3. Wheels off the ground, motors running. Carry the pad out of range - round a corner, or thirty feet down the corridor - and watch the wheels stop. Walk back and it picks up again.
  Neither of these pads has an off switch, so out of range is how you prove the failsafe. Power-cycling the VEHICLE shows the same guard from the other side: the pad is on, the sticks work, and nothing moves until it reconnects.
Notes: (Continued from the previous slide - the same notes apply.)
Step 1 is not optional. Wheels off the ground, check up is forward and right is right, every single upload.
Step 3 is the failsafe demonstration, and it needs setting up. Kevin caught this in the 2026-09-08 review: the slide used to say switch the pad off, and neither of these controllers CAN be switched off by hand. Walking out of range is the demonstration that actually works.
Send one person down the corridor with the pad while the rest of the group watches the wheels. Thirty feet, or one wall, is usually enough. If the room is small, power-cycle the vehicle instead and push the stick while it is disconnected - same guard, seen from the other side.
Steps 5 and 6 are deliberate breakages, and the line numbers on the slide are read out of the sketch when the deck is built, so they are right for the track in front of you.
Swapped signs give a vehicle that steers backwards. Dropping the turn term from the right side only gives something that swings wide one way and barely turns the other - the left wheels still get forward + turn while the right ones get forward alone.
Make them put both back before they leave.
Give this the full thirty minutes. It is the payoff for three lessons of groundwork.
ANSWER: the wheels stopped within about a second of the link dropping, and picked up again when the pad came back in range. The four lines are the if at the very top of loop(): no controller, so drive(0, 0) and return before anything else runs.

## Slide 24: Do it now - drive it (continued)
Pathfinder Beginner - PS3 | Lesson 3
24
UPLOAD AND RUN: l3c_tank_drive
4. Set turnMax to MOTOR_MAX. Which is easier to aim?
5. Lines 173 and 174: swap the + and the - and drive. What is wrong now?
6. Line 174: make it rightSpeed = forward; with no turn term. Why is that worse steering?
SAFETY Check the controls with the wheels off the ground first. Every time you upload a change.
Notes: (Continued from the previous slide - the same notes apply.)
Step 1 is not optional. Wheels off the ground, check up is forward and right is right, every single upload.
Step 3 is the failsafe demonstration, and it needs setting up. Kevin caught this in the 2026-09-08 review: the slide used to say switch the pad off, and neither of these controllers CAN be switched off by hand. Walking out of range is the demonstration that actually works.
Send one person down the corridor with the pad while the rest of the group watches the wheels. Thirty feet, or one wall, is usually enough. If the room is small, power-cycle the vehicle instead and push the stick while it is disconnected - same guard, seen from the other side.
Steps 5 and 6 are deliberate breakages, and the line numbers on the slide are read out of the sketch when the deck is built, so they are right for the track in front of you.
Swapped signs give a vehicle that steers backwards. Dropping the turn term from the right side only gives something that swings wide one way and barely turns the other - the left wheels still get forward + turn while the right ones get forward alone.
Make them put both back before they leave.
Give this the full thirty minutes. It is the payoff for three lessons of groundwork.
ANSWER: the wheels stopped within about a second of the link dropping, and picked up again when the pad came back in range. The four lines are the if at the very top of loop(): no controller, so drive(0, 0) and return before anything else runs.

## Slide 25: Failsafe: what a robot does when it stops hearing you
Pathfinder Beginner - PS3 | Lesson 3
25
A radio link is not reliable. Batteries go flat, people walk between the pad and the vehicle, and an operator walks further than the radio reaches.
The only safe behavior is to STOP. Not carry on with the last command, and not do something clever.
Three lines at the top of loop() do it:
  if (!connected) { drive(0, 0); return; }
This is not a Pathfinder detail. Every unmanned vehicle has a failsafe, and what it should do when the link drops is a real engineering decision. A drone hovers, or returns home. A submersible surfaces. A ground vehicle stops.
Ask yourself, on any system you build: what happens when the operator disappears?
SAFETY If you take one habit away from this course, take this one.
Notes: Slow down. This is the most transferable idea in the whole course.
The only safe behavior is to stop. Not to carry on with the last command, and not to be clever.
Go round the examples: a drone hovers or returns home, a submersible surfaces, a ground vehicle stops. Ask why each is right for that vehicle.
End with the question on the slide and let it sit: on anything you ever build, what happens when the operator disappears?

## Slide 26: When it will not connect
Pathfinder Beginner - PS3 | Lesson 3
26
Symptom | Most likely cause | What to do
Nothing connects at all | PS3_MAC_ADDRESS still ends in 00, or is not your number | Put the number from your controller's sticker in
Connects, then drops | Flat controller battery | Charge it over USB for a few minutes
Somebody else's vehicle moves | Two vehicles on one address | Give every vehicle a different address
Wheels spin the wrong way | Motor pins swapped | Swap that motor's two pin numbers in the sketch
It creeps with the stick centered | Deadzone too small | Raise STICK_DEADZONE
Nothing at all, no serial output | Wrong board selected | Check the board menu - see Lesson 1
Compile error: esp_base_mac_addr_set | The ORIGINAL PS3 library is installed | Uninstall it; keep only the Fork
Notes: Do not read this table out. Point at it and tell them to use it during the activity.
Worth printing and taping to the wall for the rest of the course.
Row three - somebody else's vehicle moving - is the funny one and the one that will actually happen.

## Slide 27: Check yourself
Pathfinder Beginner - PS3 | Lesson 3
27
Next lesson: the 32 LEDs, and what color actually is.
1. What is a Bluetooth address, and why must every vehicle in the room have a different one?
2. Push the left stick fully forward. Is the number positive or negative? Why does the program put a minus sign in front of it?
3. What is a deadzone for? What goes wrong if it is 0? What goes wrong if it is far too big?
4. In your own words, what does map() do?
5. forward is 180 and turn is 100. What speed does each side get, before and after constrain()?
6. Why is steering limited to 75% of full power by default?
7. Write the three lines that stop the vehicle when the controller disconnects.
Notes: Conversation, not a test.
Answers, in order: an address is the device's phone number and duplicates mean one pad drives two vehicles; the number is negative, hence the minus sign; a deadzone stops phantom creep, zero means it creeps and too big wastes the stick; map() is proportion.
For question 5: left gets 280 and right gets 80 before constrain, then 255 and 80 after.
For question 6: full-power steering is faster than a person can correct for.
The answer to question 7, in full: if (!Ps3.isConnected()) { drive(0, 0); return; } - four lines if you count the closing brace, and they go at the very top of loop().
Question 7 should be written out, not said. Check a few notebooks.