## Slide 1
LESSON 2
Motors, Resolution and Ramping
Resolution against frequency, four states of an H-bridge, fast decay, and a ramp that used to stall one count short.
PORPOISE ROBOTICS - Precision Oceanographic Program On and In the Sea Environment
porpoiserobotics.org
Kevin Bowen, President - kbowen6@icloud.com
Malcom Graham, VP Education Louis Parker, VP Technology
Valen Farre, System Engineer Gary Howland, Animation
Eddie Revollo, Artificial Intelligence
Interns: Oscar Canazales, Krishnansh Vemulapalli, Soham Gangal, Erik Olsen
Three hours. Wheels off the ground throughout.
Porpoise Robotics - proprietary. For use with Porpoise Robotics lessons.
Notes: Blocks on every desk. Everything today runs a motor at up to full power and none of it should touch the floor.
Have a multimeter to hand for the voltage column in the first activity.

## Slide 2: What you will be able to do by the end
Pathfinder Advanced - Op Program 12 | Lesson 2
2
By the end of this lesson you will be able to:
1. Work out the maximum PWM frequency for a given resolution, and say what more resolution buys you
2. Describe the four states of an H-bridge and what the motor does in each
3. Explain why fast decay holds speed better under load than slow decay
4. Spot the integer-truncation bug in a ramp, and fix it
5. Explain why remap_axis constrains before it maps
Notes: Objective four - spotting the truncation bug - is the one they will remember. It is a real bug from a real program.

## Slide 3: Today, in order
Pathfinder Advanced - Op Program 12 | Lesson 2
3
Time | What we do
0:00 | Recap. The LEDC peripheral and what it can actually do
0:25 | Resolution against frequency. Upload a2a_pwm_resolution
1:00 | BREAK (10 minutes)
1:10 | Coast, brake, and the two decay modes
1:40 | Upload a2b_coast_brake_hybrid. Feel the difference
2:10 | BREAK (10 minutes)
2:20 | Speed ramping, and the truncation bug
2:35 | remap_axis: deadzones, scale, and per-axis tuning
2:50 | Four servos on one thumbstick
Notes: Two breaks. The first activity is thirty-five minutes and it earns them; do not compress it.

## Slide 4: The LEDC peripheral, and the trade you cannot avoid
Pathfinder Advanced - Op Program 12 | Lesson 2
4
What the bits buy
Sixteen hardware channels, from an 80 MHz clock. At N bits the duty range is 0 to 2^N - 1.
  8 bits 0..255 0.39% per step
  10 bits 0..1023 0.098% per step
  12 bits 0..4095 0.024% per step
Finer control at the BOTTOM of the range, which is where a motor is hardest to drive smoothly.
What they cost
The counter has to run 2^N times per cycle, so resolution comes straight out of frequency:
  max frequency = 80,000,000 / 2^bits
  8 bits 312 kHz
  10 bits 78 kHz
  12 bits 19.5 kHz
Op 12 runs 10 bits at 30 kHz: inside the limit, above hearing, four times the beginner resolution.
WATCH OUT ledcSetup() returns the frequency it managed, or 0 if the combination is impossible. Check it.
Notes: This is a genuine engineering trade-off, so present it as one rather than as a fact to memorise.
Ten bits at the bottom of the range is the difference between a smooth start and a visible staircase. Say that - it is why the extra resolution was worth buying.
If ledcSetup() returns 0 you get silence and no error, which is a horrible thing to debug. Tell them to check the return value every time.
More bits buys finer control at the BOTTOM of the range, which is exactly where a motor is hardest to drive smoothly.
The cost is frequency: the counter has to run 2^N times per cycle. Do the division on the board.
Op 12 sits at 10 bits and 30 kHz. Ask them to check that against the formula before you confirm it.
Connect it back: the beginner course ran 8 bits, and this is what the extra two bits are for.

## Slide 5
Pathfinder Advanced - Op Program 12 | Lesson 2
5
Resolution
About 35 minutes
The LEDC peripheral
done
Resolution
NOW
Decay and ramping
Notes: Twenty seconds. First activity.

## Slide 6: Do it now - resolution you can hear
Pathfinder Advanced - Op Program 12 | Lesson 2
6
UPLOAD AND RUN: a2a_pwm_resolution (35 minutes)
1. Wheels off the ground. Upload. Type help.
2. Run step at 8 bits. Watch the volts column and LISTEN at the very bottom of the range.
3. bits 10, then step again. Compare.
4. Try bits 12 then freq 30000. Read what the console tells you.
5. Find the lowest pct at which the wheel turns at all. Is it the same at 8 bits and at 10?
6. freq 300, listen, then freq 20000.
What you should see
A duty value, a percentage, and an approximate voltage for each step of the sweep.
Answer these
Why does 12 bits at 30 kHz get refused?
Does more resolution change the lowest speed the motor will turn at, or only how finely you can approach it?
SAFETY Wheels off the ground. This reaches full power.
Notes: The console is the tool for the whole activity. Make sure everybody has typed help and got a response before moving on.
Step 2 and 3 are a listening exercise as much as a reading one. The bottom of the range is where the difference lives.
Step 4 is refused by the console on purpose. 12 bits caps out at 19.5 kHz, so 30 kHz is impossible - and the console says so rather than silently doing something else.
The second question is the subtle one: more resolution does NOT lower the speed at which the motor starts turning. It only lets you approach it more finely.

## Slide 7: The H-bridge: four switches, four things a motor can do
Pathfinder Advanced - Op Program 12 | Lesson 2
7
A high, B low
FORWARD
driven one way
A low, B high
REVERSE
driven the other way
both low
COAST
terminals floating,
motor freewheels
both high
BRAKE
terminals shorted,
motor stops hard
The arrows are the current: in at + V, along the top, down the left, through the motor, back to GND. That is the FORWARD box above. Turn pin B on instead of pin A and it all runs backwards.
Notes: Four boxes across the top: those are the four things the motor can be told to do. The picture underneath is ONE of them actually happening - the first one - drawn by Kevin.
Say that before anybody asks why they can only see two switches in the picture. The other two are the ones that are open.
Then trace the arrows with a finger on the projected slide, slowly, all the way round: in at + V, along the top, down the left, through the motor, back to GND. Have them do it too.
Ask what happens if you close both switches on one side. Somebody will work out that it shorts the supply - which is exactly why the driver chip will not let you.
Forward and reverse are the same circuit with the current running the other way. That is the whole trick, and it is why direction costs nothing extra in the program.
Brake and coast are worth ten seconds each here; they come back properly in the advanced course.

## Slide 8
Pathfinder Advanced - Op Program 12 | Lesson 2
8
Decay and ramping
About 75 minutes
The LEDC peripheral
done
Resolution
done
Decay and ramping
NOW
Notes: Twenty seconds. Second activity.

## Slide 9: Slow decay against fast decay
Pathfinder Advanced - Op Program 12 | Lesson 2
9
Sign-magnitude (the beginner programs)
Pulse IN1 at the duty you want. Hold IN2 low.
The motor alternates between DRIVEN and COAST.
During the off part nothing controls the motor at all, so the current in the windings decays slowly and the actual speed depends heavily on the load.
Simple to read, and perfectly good for learning.
This is SLOW DECAY.
Hybrid drive (Op Program 12)
Hold IN1 HIGH. Pulse IN2 at the inverse of the duty.
The motor alternates between DRIVEN and BRAKE.
The braking part actively pulls the current down, so the average is much closer to what you asked for, and speed holds up under load.
Noticeably better control at low duty - exactly where you need it.
This is FAST DECAY.
WATCH OUT Watch the zero case. In hybrid, duty 0 puts PWM_MAX on BOTH pins, which is a hard brake, not a coast. Op 12 tests for zero separately and calls coast_all(). Miss that and the vehicle will not roll when you let go.
Notes: Both columns describe the same H-bridge. What changes is what happens during the off part of each cycle.
Sign-magnitude alternates driven and coast. Hybrid alternates driven and brake, which actively pulls the current down.
The practical consequence: hybrid holds the speed you asked for when the load changes. They will feel this in the activity.
Sign-magnitude is not wrong. It is simpler to read, and that is why the beginner programs use it.

## Slide 10: Hybrid drive, and the trap in it
Pathfinder Advanced - Op Program 12 | Lesson 2
10
Motors.ino
void set_motor_hybrid(uint8_t in1_ch, uint8_t in2_ch, int duty) {
duty = constrain(duty, -PWM_MAX, PWM_MAX);
if (duty == 0) { // WITHOUT THIS, ZERO IS A BRAKE
ledcWrite(in1_ch, 0);
ledcWrite(in2_ch, 0);
return;
}
int inverse = PWM_MAX - abs(duty);
if (duty > 0) {
ledcWrite(in1_ch, PWM_MAX);
ledcWrite(in2_ch, inverse);
} else {
ledcWrite(in1_ch, inverse);
ledcWrite(in2_ch, PWM_MAX);
}
}
Full duty forward: IN1 = 1023, IN2 = 0. Driven hard.
Half duty forward: IN1 = 1023, IN2 = 512. Half driven, half braked.
Zero without the guard: IN1 = 1023, IN2 = 1023. Both high. That is a brake.
A vehicle that will not coast, and cannot be pushed by hand when it is switched on, has this bug.
Notes: Walk the three cases on the right-hand notes before reading the code.
The guard clause is the whole slide. Without it, duty zero puts both pins high, and both pins high is a brake.
Ask what that feels like: a vehicle that will not coast and cannot be pushed by hand when switched on. That is a real symptom somebody would report as a mechanical fault.
This is a good example of a bug that hides in the ONE case the arithmetic happens to handle differently.

## Slide 11: The ramp, and the bug that hid in it for a year
Pathfinder Advanced - Op Program 12 | Lesson 2
11
Motors.ino
// Op 11.2 wrote this:
current += (target - current) * RAMP_FACTOR;
// With RAMP_FACTOR = 0.5 and a gap of 1:
// 1 * 0.5 = 0.5, truncated to 0
// -> current never changes again
// -> the ramp stalls ONE COUNT short, forever
// Op 12:
int ramp_towards(int current, int target) {
int gap = target - current;
if (gap == 0) return current;
int step = (int)(gap * RAMP_FACTOR);
if (step == 0) step = (gap > 0) ? 1 : -1; // the fix
return current + step;
}
Ramping stops the vehicle lurching and stops it yanking a large current out of the battery on every stick movement.
Closing a FRACTION of the gap each step gives a smooth exponential approach - fast at first, gentle at the end.
The bug is invisible. One count out of 1023 is 0.1% of full power. Nobody would ever see it on a wheel.
It matters because comparisons against the target then never become true, and anything waiting for "ramp finished" waits forever.
Notes: Set the scene: this bug lived for a year in shipping code.
Do the arithmetic out loud. Gap of 1, factor of 0.5, gives 0.5, which truncates to 0 - so current never changes again.
The ramp stalls one count short, forever. On a 1024-count scale that is 0.1%, which nobody can see on a wheel.
Ask why it still matters. Because a value that never reaches its target breaks anything that tests for equality, and because a bug you cannot see is worse than one you can.
The fix is one line: if the step rounds to nothing, take one count.

## Slide 12: Do it now - decay modes and ramping
Pathfinder Advanced - Op Program 12 | Lesson 2
12
UPLOAD AND RUN: a2b_coast_brake_hybrid (35 minutes)
1. sign, then go 100. Pinch the tire gently.
2. hybrid, then go 100. Pinch again. Which holds speed?
3. Find the lowest go that turns the wheel in each mode.
4. ramp off, then go 1023 from a standstill. Then ramp on and repeat. Listen to the difference.
5. Set RAMP_FACTOR to 0.9, then 0.1. What changes?
6. DELETE the minimum-step line in ramp_towards and run go 500. Watch where the printout stops.
What you should see
Step 6: the ramp prints down to one count short of the target, then stops.
Answer these
Why does fast decay hold speed better under load?
Why would a 0.1% speed error still be a real bug?
SAFETY Wheels off the ground. One motor, up to full power.
Notes: Steps 1 and 2 are a feel test. Pinching the tire gently is the load - warn them to be gentle and to keep fingers clear of the spokes.
Step 6 recreates the bug deliberately. Watching the printout stop one count short is the memorable part of this lesson.
Answer to the first question: fast decay actively pulls the winding current down during the off part, so the average tracks the command.
Answer to the second: a 0.1% error is invisible but it means a value that never reaches its target, and anything comparing for equality never fires.

## Slide 13: Pulse width modulation: how a pin makes a half speed
Pathfinder Advanced - Op Program 12 | Lesson 2
13
25% duty
quarter power
ledcWrite(pin, 64)
50% duty
half power
ledcWrite(pin, 128)
100% duty
full power
ledcWrite(pin, 255)
one cycle = 1/20000 s; this picture repeats 5000 times a second
KEY POINT The pin is only ever fully on or fully off. Speed comes from the FRACTION of each cycle it spends on - the duty cycle.
Notes: Draw the square wave on the board first, then reveal the slide. It lands better if they have watched it being built.
The idea to land: the pin is only ever fully on or fully off. Half speed is half the TIME on, not half the voltage.
Analogy that works: a light switch flicked very fast. Too fast to see flicker, so the room looks half lit.
Duty cycle is a percentage, which is why the math lesson and the motor lesson are the same lesson.

## Slide 14: remap_axis: deadzone, scale, and range, in one function
Pathfinder Advanced - Op Program 12 | Lesson 2
14
Motors.ino
int remap_axis(int raw_value, int specific_dz, float scale_factor,
int in_max, int out_max) {
int dz = get_effective_deadzone(specific_dz);
if (abs(raw_value) < dz) return 0;
int sign = (raw_value > 0) ? 1 : -1;
int scaled = lround(abs(raw_value) * scale_factor);
scaled = constrain(scaled, dz, in_max);
return sign * map(scaled, dz, in_max, 0, out_max);
}
A per-axis deadzone of -1 means "use the global one" - a default and an override, with no second flag.
lround(), not a cast, so 0.5 rounds up rather than truncating. The same class of bug as the ramp.
constrain() BEFORE map(): map() does not clamp.
Sign comes off at the start and goes back on at the end.
Notes: Four ideas in ten lines. Take them one at a time.
The -1 sentinel for a per-axis deadzone gives you a default and an override with no second flag. That is a pattern worth naming.
lround() rather than a cast, so 0.5 rounds up. Point out that this is the SAME class of bug as the ramp, avoided this time.
constrain() before map(), because map() does not clamp. Ask what happens if you do it the other way round.
Sign comes off at the start and goes back on at the end, so the math in the middle only ever deals with positive numbers.

## Slide 15: Throttle modes, and four servos on one stick
Pathfinder Advanced - Op Program 12 | Lesson 2
15
Throttle modes (L3 toggles)
NORMAL - full forward speed, steering scaled to 0.75.
FAST - full forward speed, full steering authority.
Only the STEERING scale changes. Top speed is the same in both.
This matters: it was the steering that needed softening, not the speed. A global speed cap makes a vehicle feel broken; a steering cap makes it feel controllable.
Four servos, one right stick
Each servo owns one DIRECTION of the stick, and pushing that way moves it from center to one end, about 90 degrees:
  servo 1 - stick up
  servo 3 - stick down
  servo 2 - stick left
  servo 4 - stick right
Each sits centered whenever the stick is not pushed its way, so one stick aims four independent things.
Travel is 1.0 to 2.0 ms. 11.2 used 0.5 to 2.5, which can drive a servo into its mechanical end stops.
Notes: The left column is a design argument, not a feature list. Only the steering scale changes between the modes.
The reasoning is worth hearing: a global speed cap makes a vehicle feel broken, a steering cap makes it feel controllable. Ask whether they agree.
The four-servo scheme surprises people. One stick, four servos, each owning one direction and centered otherwise.
1.0 to 2.0 ms is the corrected travel. Point back to the change log in Lesson 1 - the old range could drive a servo into its stops.

## Slide 16: A servo listens to the LENGTH of a pulse
Pathfinder Advanced - Op Program 12 | Lesson 2
16
1.0 ms
one end of the travel
1.5 ms
centered
2.0 ms
the other end
the whole cycle is 20 ms, repeated 50 times a second
The ESP32 counts duty, not microseconds. At 16-bit resolution one 20 ms cycle is 65536 counts:
duty = microseconds * 65536 / 20000
Notes: A servo does not listen to voltage, or to duty in the way a motor does. It listens to how LONG the pulse is, and it wants one every 20 ms.
1.0 ms is one end, 1.5 ms is center, 2.0 ms is the other end. Those three numbers are the whole protocol.
The ESP32 counts duty, not microseconds, so the program has to convert. Walk the arithmetic once, slowly.
Continuous-rotation servos read the same pulse as a SPEED rather than a position. Worth flagging before somebody buys the wrong one.

## Slide 17: Check yourself
Pathfinder Advanced - Op Program 12 | Lesson 2
17
Next lesson: identity that survives a power cycle.
1. Why can you not have 12-bit resolution at 30 kHz on this chip?
2. What does more PWM resolution actually buy you, and where?
3. Describe the four states of an H-bridge and what the motor does in each.
4. Why does hybrid drive hold speed better under load?
5. In hybrid drive, what happens at duty 0 without the guard clause?
6. Explain the ramp truncation bug, and why nobody would see it on a wheel.
7. Why does remap_axis call constrain() before map() rather than after?
8. Why does NORMAL mode scale steering rather than top speed?
Notes: Conversation, not a test.
Answers: 12 bits caps at 19.5 kHz because 80 MHz divided by 4096 is 19,531; resolution buys fine control at the bottom of the range; the four states are forward, reverse, coast and brake.
Hybrid drive holds speed because the braking part actively pulls current down. At duty 0 without the guard, both pins go high and the motor brakes.
The truncation bug leaves the ramp one count short, which is 0.1% and invisible on a wheel.
constrain before map because map does not clamp. NORMAL scales steering because steering authority was the problem, not top speed.