## Slide 1
LESSON 4
The Lighting State Machine
Six modes, one variable, no delay() anywhere, and geometry that is not symmetric.
PORPOISE ROBOTICS - Precision Oceanographic Program On and In the Sea Environment
porpoiserobotics.org
Kevin Bowen, President - kbowen6@icloud.com
Malcom Graham, VP Education Louis Parker, VP Technology
Valen Farre, System Engineer Gary Howland, Animation
Eddie Revollo, Artificial Intelligence
Interns: Oscar Canazales, Krishnansh Vemulapalli, Soham Gangal, Erik Olsen
Three hours. Nothing moves today.
Porpoise Robotics - proprietary. For use with Porpoise Robotics lessons.
Notes: Nothing moves today, so no blocks needed. Dim the room if you can.
Have a vehicle in front of you with the LED map from the beginner course to hand. The geometry section needs it.

## Slide 2: What you will be able to do by the end
Pathfinder Advanced - Op Program 12 | Lesson 4
1
By the end of this lesson you will be able to:
1. Say why a state machine beats a set of booleans for lighting
2. Write a non-blocking animation that draws one frame per pass
3. Explain what a dirty flag saves, and measure it
4. Work out the LED indices for a turn signal on either side
5. Add a new lighting mode without touching the existing ones
Notes: The last objective is the assessment: adding a mode without touching the existing ones is what a good architecture buys you.

## Slide 3: Today, in order
Pathfinder Advanced - Op Program 12 | Lesson 4
2
Time | What we do
0:00 | Recap. What a state machine buys you
0:25 | The six modes, and how control passes between them
0:50 | Non-blocking animation as a discipline
1:10 | Upload a4a_led_state_machine. Measure a redraw
1:40 | BREAK (10 minutes)
1:50 | Colour helpers, and why they are written out longhand
2:10 | Turn signal geometry. Upload a4b_turn_signal_larson
2:35 | BREAK (10 minutes)
2:45 | Add a mode of your own
Notes: Two breaks. The final thirty minutes is a build exercise - protect it.

## Slide 4: Why lighting needs a state machine and not a pile of booleans
Pathfinder Advanced - Op Program 12 | Lesson 4
3
Six booleans is 64 combinations. One enum is six.
Suppose you track lighting with flags: lights_on, turning_left, turning_right, scanning, pairing, disconnected.
Six booleans is 64 combinations. Most are nonsense - turning left AND right, pairing AND driving - and every one of them is reachable by a bug.
A STATE MACHINE says: the vehicle is in exactly ONE mode. One variable holds it. Each mode knows how to draw itself and when to hand over.
Two things fall out:
  Two modes can never be half-on at once, because there is one variable and it holds one value.
  Adding a mode is one enum value and one branch - not a new combination to test against every existing flag.
  enum LEDMode { DISCONNECTED, STANDBY, TURN_LEFT, TURN_RIGHT,
  PAIRING, KITT_SCANNER };
Notes: Do the arithmetic on the board: six booleans is 64 combinations, and most of them are nonsense that a bug can still reach.
Turning left AND right at the same time is the example that lands. Ask what the lights would actually do.
One variable, one value, so two modes can never be half-on at once. That is not discipline, it is structure.
The second consequence is the one they will test at the end of the lesson: adding a mode is one enum value and one branch.

## Slide 5: The lighting state machine
Pathfinder Advanced - Op Program 12 | Lesson 4
4
DISCONNECTED
green pulse
no controller
PAIRING
blue breathing
waiting to pair
STANDBY
headlights + tail lights
redrawn only when dirty
TURN_LEFT
amber bar, 3 cycles
TURN_RIGHT
amber bar, 3 cycles
KITT_SCANNER
sweeping dot, 3 cycles
controller connects
D-pad or button
each animation counts its own cycles and hands itself back
KEY POINT One variable holds the mode, so two modes can never be half-on at once. Adding a mode is one enum value and one branch - not a new combination of flags to test.
Notes: A state machine is just: what am I doing now, and what could make that change. The diagram is a picture of exactly that.
Point out that exactly one state is active at a time. That is what stops the lights contradicting themselves.
Ask the room for a transition that is missing, then decide together whether it should be there.
This shape turns up everywhere in embedded work. Naming it now means they recognise it later.

## Slide 6: Non-blocking, as a rule with no exceptions
Pathfinder Advanced - Op Program 12 | Lesson 4
5
One frame per pass, never a loop that waits
Not one animation function in Op 12 calls delay(). Each checks the clock, returns immediately if it is not time, and draws exactly ONE frame when it is:
  if (now - last_update < INTERVAL) return;
  last_update = now;
  // ...draw one frame...
That is what lets the vehicle drive, read its controller, watch its current and animate all at the same time.
Notes: This is the beginner-course millis() pattern, promoted to a rule with no exceptions.
Three lines: is it time, remember when, draw ONE frame. Get them to say it back.
The System Test story is the counterexample. A vehicle that keeps driving while it ignores you is a safety problem, not a cosmetic one.
The one legitimate delay() is the startup show, because nothing else needs to happen yet. Being able to say exactly why the exception is allowed is the mark of understanding the rule.

## Slide 7: Non-blocking, as a rule with no exceptions (continued)
Pathfinder Advanced - Op Program 12 | Lesson 4
6
The old System Test program did the opposite: a light pattern with delay() in it froze the vehicle for two seconds, still holding whatever motor command was last set. A vehicle that keeps driving while it ignores you is not a cosmetic problem.
The one legitimate delay() in the whole program is the startup light show, because nothing else needs to happen yet.
KEY POINT "Draw one frame and return" is the same discipline a game engine uses. Once you see it, you will see it everywhere.
Notes: (Continued from the previous slide - the same notes apply.)
This is the beginner-course millis() pattern, promoted to a rule with no exceptions.
Three lines: is it time, remember when, draw ONE frame. Get them to say it back.
The System Test story is the counterexample. A vehicle that keeps driving while it ignores you is a safety problem, not a cosmetic one.
The one legitimate delay() is the startup show, because nothing else needs to happen yet. Being able to say exactly why the exception is allowed is the mark of understanding the rule.

## Slide 8: Dirty flags: not redrawing for nothing
Pathfinder Advanced - Op Program 12 | Lesson 4
7
Lighting.ino
// STANDBY is not an animation. It is ONE PICTURE that changes
// only when the headlights or running lights change.
void set_standby_lighting() {
strip.clear();
if (running_lights_on) {
uint8_t level = full_headlights ? HEADLIGHT_BRIGHT
: HEADLIGHT_DIM;
fill_range(LEFT_FRONT_START, CORNER_LEN * 2, rgb(level, level, level));
fill_range(RIGHT_REAR_START, CORNER_LEN * 2, rgb(TAILLIGHT_LEVEL, 0, 0));
}
strip.show();
standby_dirty = false; // <- the whole point
}
// ...and the last branch of update_lighting():
if (led_mode == STANDBY && standby_dirty) {
set_standby_lighting();
}
Pushing 32 WS2812B pixels takes about 1 ms of tightly timed bit-banging. loop() runs tens of thousands of times a second.
11.2 pushed standby lighting on EVERY pass. That is most of the vehicle's attention, spent redrawing an identical picture.
Anything that alters the picture sets standby_dirty = true. The state machine clears it.
Graphics engines, spreadsheets and browsers all do this. Anywhere redrawing is expensive, something is tracking what actually changed.
Notes: STANDBY is not an animation. It is one picture that changes only when something changes it. Make that distinction clearly.
One line - clearing the flag - is what turns a redraw every pass into a redraw when it matters.
They measure exactly what that line is worth in the next activity, so do not give them the number now.
Pushing 32 pixels is about a millisecond of tightly timed bit-banging. That is why it is expensive.

## Slide 9: Where we are
Pathfinder Advanced - Op Program 12 | Lesson 4
8
State machines
done
Measuring a redraw
NOW
Turn signal geometry
Notes: Twenty seconds. First activity.

## Slide 10: Do it now - measure the state machine
Pathfinder Advanced - Op Program 12 | Lesson 4
9
UPLOAD AND RUN: a4a_led_state_machine (35 minutes)
1. Upload. Switch between the four modes from the console.
2. Type load in each mode. Which mode costs the most time per pass? Why?
3. In standby, type bright and dim. Watch WHEN the redraw happens.
4. Comment out the standby_dirty = false at the end of setStandbyLighting. Upload. Check load in standby again.
5. Write down both numbers. That is what one line was worth.
6. Add a fifth mode: ALARM, a slow red pulse.
What you should see
A large loop count in standby, and a much smaller one once the dirty flag is removed.
Answer these
How many passes per second in standby with the flag? Without it?
What did you have to change to add ALARM? How many places?
Notes: The load command is the instrument for this whole activity. Make sure everybody gets a reading before step 4.
Step 4 removes the dirty flag on purpose, and step 5 makes them write down both numbers. That comparison IS the lesson.
Step 6 - adding an ALARM mode - is a rehearsal for the exercise at the end. Note how few places they had to touch.
Thirty-five minutes. If a group finishes early, ask them to add a second mode and check the cost is the same.

## Slide 11: Colour helpers, written out longhand
Pathfinder Advanced - Op Program 12 | Lesson 4
10
What 11.2 got from FastLED
CRGB, fill_solid(), nscale8(), sin8() - all free.
Op 12 cannot use FastLED: version 3.10.5 auto-enables an ESP-DSP FFT backend, and the bluepad32 SDK ships that header without the include directory it needs. There is no per-sketch opt-out.
So the handful of helpers we actually relied on are written out in Lighting.ino.
Why that turned out to be a good thing
scale_colour() unpacks a 32-bit colour into three bytes, scales each, and repacks it. Four lines, and now the bit-shifting is visible instead of magic.
sine8() maps 0..255 of angle onto 0..255 of amplitude with 128 as the midpoint. Two lines of floating point.
Notes: The FastLED story is a real dependency failure and worth telling properly: a minor version auto-enabled a backend that would not build against the SDK, with no per-sketch opt-out.
Then make the constructive point. Writing the four helpers out by hand made the bit-shifting visible instead of magic.
The line to land: a dependency you do not understand is a dependency that will eventually break in a way you cannot fix.
That is not an argument against libraries. It is an argument for knowing what the ones you rely on actually do.

## Slide 12: Colour helpers, written out longhand (continued)
Pathfinder Advanced - Op Program 12 | Lesson 4
11
Why that turned out to be a good thing (cont.)
A dependency you do not understand is a dependency that will eventually break in a way you cannot fix. Forty lines of your own code is often the cheaper option.
KEY POINT It also means the whole course - beginner and advanced - now uses one LED library instead of two.
Notes: (Continued from the previous slide - the same notes apply.)
The FastLED story is a real dependency failure and worth telling properly: a minor version auto-enabled a backend that would not build against the SDK, with no per-sketch opt-out.
Then make the constructive point. Writing the four helpers out by hand made the bit-shifting visible instead of magic.
The line to land: a dependency you do not understand is a dependency that will eventually break in a way you cannot fix.
That is not an argument against libraries. It is an argument for knowing what the ones you rely on actually do.

## Slide 13: Turn signal geometry, which is the genuinely hard part
Pathfinder Advanced - Op Program 12 | Lesson 4
12
Two bars, four directions, one loop of wire
The strip is one loop, so the two halves of each side run in OPPOSITE directions and the arithmetic is not symmetric:
  front, left to right : 0 .. 15 left half 0-7, right half 8-15
  rear, right to left : 16 .. 31 right half 16-23, left half 24-31
The bar has to grow OUTWARD from the centre of the vehicle towards the corner that is turning, on both bars at once.
LEFT signal:
  front: RIGHT_FRONT_START - 1 - i (counts DOWN from 7)
  rear: LEFT_REAR_START + i (counts UP from 24)
Notes: This is the hardest slide in the lesson. Have a real vehicle out and point at LEDs while you talk.
The strip is ONE loop, so the two halves of each side run in opposite directions. That is the whole reason the arithmetic is asymmetric.
The bar grows outward from the centre towards the turning corner, on both bars at once. Trace it with a finger before showing the indices.
Take the advice on the slide seriously: do not derive it. Step through it and read the numbers off a real vehicle. They do exactly that in the activity.

## Slide 14: Turn signal geometry, which is the genuinely hard part (continued)
Pathfinder Advanced - Op Program 12 | Lesson 4
13
RIGHT signal:
  front: RIGHT_FRONT_START + i (counts UP from 8)
  rear: LEFT_REAR_START - 1 - i (counts DOWN from 23)
Do not try to derive this. Step through it and read the indices.
Notes: (Continued from the previous slide - the same notes apply.)
This is the hardest slide in the lesson. Have a real vehicle out and point at LEDs while you talk.
The strip is ONE loop, so the two halves of each side run in opposite directions. That is the whole reason the arithmetic is asymmetric.
The bar grows outward from the centre towards the turning corner, on both bars at once. Trace it with a finger before showing the indices.
Take the advice on the slide seriously: do not derive it. Step through it and read the numbers off a real vehicle. They do exactly that in the activity.

## Slide 15: Two details that are easy to miss
Pathfinder Advanced - Op Program 12 | Lesson 4
14
Lighting.ino
// 1. Repaint the BASE lighting first, every frame.
strip.clear();
if (running_lights_on) {
fill_range(LEFT_FRONT_START, CORNER_LEN * 2, headlights);
fill_range(RIGHT_REAR_START, CORNER_LEN * 2, taillights);
}
// ...then blank the signalling side, then draw the amber over it.
// Painting only the amber would leave the last frame underneath.
// 2. The animation finishes its own cycles.
bool still_held = (led_mode == TURN_LEFT && (dpad & DPAD_LEFT)) ||
(led_mode == TURN_RIGHT && (dpad & DPAD_RIGHT));
if (!still_held && turn_signal_cycles >= TURN_CYCLES) {
led_mode = STANDBY;
standby_dirty = true;
}
The D-pad only ever STARTS the animation. It does not hold it on and it does not stop it.
A real indicator does not stop mid-blink when you let go of the stalk. It finishes.
Holding the D-pad keeps resetting the count, so it carries on for as long as you hold it and then finishes cleanly.
This is a small thing that makes a machine feel considered rather than twitchy.
Notes: Two details, both of which look like paranoia until you skip them.
Repainting the base first means the previous frame is not left underneath. Ask what a signal painted over a stale frame would look like.
The D-pad only STARTS the animation. It does not hold it on and it does not stop it.
That matches a real indicator, which finishes its blink after you let go of the stalk. Small detail, and it is what makes it feel right.

## Slide 16: Where we are
Pathfinder Advanced - Op Program 12 | Lesson 4
15
State machines
done
Measuring a redraw
done
Turn signal geometry
NOW
Notes: Twenty seconds. Second activity.

## Slide 17: Do it now - step through the geometry
Pathfinder Advanced - Op Program 12 | Lesson 4
16
UPLOAD AND RUN: a4b_turn_signal_larson (35 minutes)
1. Upload. Type left, then right.
2. Type speed 0 to freeze it, then step repeatedly. READ the indices it prints and check them against the vehicle.
3. hold left, wait, then release. Where exactly does it stop?
4. speed 200 and watch the bar build slowly.
5. Change the LEFT branch to use LEFT_FRONT_START + i and see what breaks. Explain it.
6. Make the trailing edge FADE rather than switch off abruptly.
What you should see
Amber growing outward from the centre towards the turning corner, front and rear mirrored.
Answer these
Why does the front index count down for a left signal but up for a right one?
What would happen if the base lighting were not repainted each frame?
Notes: Step 2 is the point of the whole activity: freeze it, step it, and read the indices against a real vehicle.
Step 5 breaks the left branch on purpose. The bar grows the wrong way, inward instead of outward, and they should be able to say why.
Step 6 is open-ended. A fading trailing edge needs scale_colour(), which they met two slides ago.
Answers: the front counts down for a left signal because the left half of the front bar is indices 0 to 7 and the growth is outward from 8; without the base repaint you would see the previous frame left underneath.

## Slide 18: The state machine itself
Pathfinder Advanced - Op Program 12 | Lesson 4
17
Lighting.ino
void update_lighting(unsigned long now, uint8_t dpad) {
if (led_mode == PAIRING) {
update_pairing_breathing(now);
return;
}
if (led_mode == TURN_LEFT || led_mode == TURN_RIGHT) {
if (now - larson_time < LARSON_DELAY_MS) return;
larson_time = now;
// ...advance one phase, count cycles, maybe hand back...
update_larson_scanner();
return;
}
if (led_mode == KITT_SCANNER) {
if (now - kitt_time < (unsigned long)KITT_SPEED_MS) return;
kitt_time = now;
// ...draw one frame, step the dot, maybe hand back...
return;
}
Every branch does the same three things: is it my turn, is it time yet, draw ONE frame.
Every branch returns. Exactly one mode runs per pass, and none of them can run into another.
The early return on the timer is what makes this cheap. Most passes through this function do almost nothing at all.
Note that STANDBY is last and has no timer - it is the fall-through, and it only acts when the dirty flag says so.
Notes: This is the whole state machine on one screen. Let them look at it in silence for thirty seconds before you say anything.
Every branch does the same three things: is it my turn, is it time yet, draw one frame. Get them to notice the repetition themselves.
The early returns are what keeps it flat and readable. Ask what this would look like as nested ifs.
Point out that STANDBY is last and is the only branch guarded by a flag rather than a clock.

## Slide 19: The state machine itself (continued)
Pathfinder Advanced - Op Program 12 | Lesson 4
18
Lighting.ino
if (led_mode == STANDBY && standby_dirty) {
set_standby_lighting();
}
}
Notes: (Continued from the previous slide - the same notes apply.)
This is the whole state machine on one screen. Let them look at it in silence for thirty seconds before you say anything.
Every branch does the same three things: is it my turn, is it time yet, draw one frame. Get them to notice the repetition themselves.
The early returns are what keeps it flat and readable. Ask what this would look like as nested ifs.
Point out that STANDBY is last and is the only branch guarded by a flag rather than a clock.

## Slide 20: Breathing, and an 8-bit sine
Pathfinder Advanced - Op Program 12 | Lesson 4
19
Why the fade is a sine and not a ramp
The pairing animation fades the whole strip up and down smoothly. Doing that with a straight line looks wrong - it appears to hover at the ends and rush through the middle.
A sine wave is what looks natural, because it slows at the extremes. FastLED gave 11.2 a sin8() for this. Op 12 writes it out:
  uint8_t sine8(uint8_t theta) {
  float radians = (theta / 256.0f) * 2.0f * PI;
  return (uint8_t)(128.0f + 127.0f * sinf(radians));
  }
Notes: Start with why a linear fade looks wrong: it appears to hover at the ends and rush through the middle.
A sine slows at the extremes, which is what your eye expects. That is a perception point, like the colour lesson in the beginner course.
The 0..255 in, 0..255 out convention keeps floating point out of the caller entirely. Worth noticing as an interface design choice.
Deriving the phase from millis() rather than a counter means the animation keeps correct time even if a frame is missed. That is the transferable idea.

## Slide 21: Breathing, and an 8-bit sine (continued)
Pathfinder Advanced - Op Program 12 | Lesson 4
20
Feed it 0..255 for one full turn, get 0..255 back with 128 as the midpoint. No angles in degrees, no floating point in the caller.
Then the phase comes from the clock rather than from a counter:
  phase = (now % BREATHE_PERIOD_MS) * 255 / BREATHE_PERIOD_MS;
Deriving the phase from millis() rather than incrementing a variable means the animation runs at the same speed no matter how often the function gets called, and it cannot drift.
KEY POINT Compute animation state FROM the clock rather than stepping a counter. It is self-correcting, and it survives a slow pass of loop() without stuttering.
Notes: (Continued from the previous slide - the same notes apply.)
Start with why a linear fade looks wrong: it appears to hover at the ends and rush through the middle.
A sine slows at the extremes, which is what your eye expects. That is a perception point, like the colour lesson in the beginner course.
The 0..255 in, 0..255 out convention keeps floating point out of the caller entirely. Worth noticing as an interface design choice.
Deriving the phase from millis() rather than a counter means the animation keeps correct time even if a frame is missed. That is the transferable idea.

## Slide 22: Add a mode - thirty minutes, in your groups
Pathfinder Advanced - Op Program 12 | Lesson 4
21
The real test of a design is what it costs to extend
Add a HAZARD mode to a4a_led_state_machine: all four corners flashing amber together, running until it is switched off.
Do it the way the program is built:
  1. Add HAZARD to the LEDMode enum.
  2. Add its timing constants to the configuration block at the top - not buried in the function.
  3. Write update_hazard(now) so it draws ONE frame and returns.
  4. Add one branch to the state machine.
  5. Add a console command to enter and leave it.
Notes: Thirty minutes, hands off. Circulate but do not solve.
The five steps are the architecture of the program, restated as a recipe. Insist on step 2 - constants at the top, not buried in the function.
The first question is the real assessment. Count the lines they had to change in existing code.
HAZARD and TURN_LEFT can never both be on, because there is one variable holding one value. Make sure somebody says that out loud.
Leave five minutes to demonstrate. Every group shows theirs.

## Slide 23: Add a mode - thirty minutes, in your groups (continued)
Pathfinder Advanced - Op Program 12 | Lesson 4
22
Then answer these:
  How many existing lines did you have to change?
  Could HAZARD and TURN_LEFT ever be on at the same time? Why not?
  What does load say while it is running?
The point of the exercise is the first question. If a new mode costs you one enum value and one branch, the design is doing its job.
Notes: (Continued from the previous slide - the same notes apply.)
Thirty minutes, hands off. Circulate but do not solve.
The five steps are the architecture of the program, restated as a recipe. Insist on step 2 - constants at the top, not buried in the function.
The first question is the real assessment. Count the lines they had to change in existing code.
HAZARD and TURN_LEFT can never both be on, because there is one variable holding one value. Make sure somebody says that out loud.
Leave five minutes to demonstrate. Every group shows theirs.

## Slide 24: Check yourself
Pathfinder Advanced - Op Program 12 | Lesson 4
23
Next lesson: a machine that tests its own hardware.
1. Six booleans give how many combinations? One six-value enum?
2. Write the three-line non-blocking animation pattern.
3. What is a dirty flag, and roughly what did it save on this vehicle?
4. Why can Op 12 not use FastLED?
5. Why does each turn-signal frame repaint the headlights?
6. Why does the front index count down for a LEFT signal?
7. Why does the turn signal finish its cycles instead of stopping when the D-pad is released?
8. You want to add a hazard-lights mode. What exactly do you have to change?
Notes: Conversation, not a test.
Answers: 64 combinations against 6; the three-line pattern should be written out; a dirty flag skips a redraw when nothing changed, and they have their own measured numbers for what it saved.
FastLED 3.10.5 auto-enables an ESP-DSP backend that will not build against the bluepad32 SDK.
Each frame repaints the headlights so the previous frame is not left underneath.
The front counts down for a left signal because the growth is outward from the centre of the bar.
The signal finishes its cycles because that is what a real indicator does.
For question 8: one enum value, one set of constants, one update function, one branch, one console command.