## Slide 1
LESSON 6
Drive by Code
No controller today. You write the moves, the vehicle drives them all by itself - and you find out how good your numbers really are.
PORPOISE ROBOTICS - Precision Oceanographic Program On and In the Sea Environment
porpoiserobotics.org
Kevin Bowen, President - kbowen6@icloud.com
Malcom Graham, VP Education Louis Parker, VP Technology
Valen Farre, System Engineer Gary Howland, Animation
Eddie Revollo, Artificial Intelligence
Interns: Oscar Canazales, Krishnansh Vemulapalli, Soham Gangal, Erik Olsen
One hour. Teams of three, one vehicle per team.
Porpoise Robotics - proprietary. For use with Porpoise Robotics lessons.
Notes: BEFORE CLASS: tape one square per team on the floor, about 4 feet on a side, with START marked. Hard floor is better than carpet for repeatable results.
Sticky notes for marking where each run ends are a big help.

## Slide 2: Today's mission
Pathfinder Explorers | Lesson 6
2
By the end of today, you can:
1. Write a program that drives the vehicle by itself
2. Measure time in milliseconds
3. Tune a number by testing, measuring, and changing one thing at a time
4. Explain why a robot that drives by the clock makes mistakes
Notes: Read them out. The third one is the real lesson of the day: tuning is a skill, and it has rules.

## Slide 3: Last time
Pathfinder Explorers | Lesson 6
3
The wheels turned - safely up on the stand.
drive(50, -50) made the vehicle spin.
Today: the FLOOR! But no controller. The vehicle drives a plan you wrote.
That's called AUTOPILOT.
Switch jobs!
Notes: Ask what drive(50, -50) does before you show the slide, and what a team's wake-up speed was.

## Slide 4: Today, in order
Pathfinder Explorers | Lesson 6
4
Time | What we do
0:00 | Warm-up: what does drive(50, -50) do?
0:05 | Autopilot moves, and milliseconds
0:13 | Upload e06a_drive_a_square and run it on the floor
0:28 | Tune TURN_TIME until it comes home
0:52 | Mission Log and pack up
Notes: Put the agenda on the board as well, with the driving or uploading block circled. Students settle when they can see when the hands-on part starts.
The timings are a guide for a one-hour session. If the hands-on block runs long, take the time out of the check yourself questions, never out of the pack-up - a rushed pack-up is how cables and controllers go missing.

## Slide 5
Pathfinder Explorers | Lesson 6
5
Autopilot
About 10 minutes
Autopilot
NOW
Drive a square
Tune it
Notes: A breath between parts of the lesson. Read the title out and point at where it sits on the strip.

## Slide 6: Autopilot moves
Pathfinder Explorers | Lesson 6
6
Every move takes a time, in MILLISECONDS.
Move | What it does
forward(1000) | Drive forward for 1000 milliseconds, then stop
backward(1000) | Drive backward for 1000 milliseconds
spinLeft(500) | Spin left on the spot for 500 milliseconds
spinRight(500) | Spin right on the spot for 500 milliseconds
pause(1000) | Stop and wait for 1000 milliseconds
countdown(5) | 5... 4... 3... 2... 1... GO! on the lights
Notes: These are all in the engine room, explorer.h. Each one runs the motors, waits, then stops.
How fast they go is set by setDriveSpeed(), which is in the program's settings.

## Slide 7: Milliseconds
Pathfinder Explorers | Lesson 6
7
A millisecond is one thousandth of a second.
1000 milliseconds = 1 second.
500 = half a second. 250 = a quarter of a second.
Why so small? Because a robot can do a LOT in one second.
KEY POINT Quick! How many milliseconds in 3 seconds? In 2 and a half?
Notes: Answers: 3000, and 2500.
A good feel for it: a blink of an eye takes very roughly 100 to 400 milliseconds. Have them blink and guess.

## Slide 8: The settings you'll tune
Pathfinder Explorers | Lesson 6
8
e06a_drive_a_square.ino, line 31
const int SPEED_LIMIT = 50; // Learner
const int DRIVE_SPEED = 60; // Percent
const int SIDE_TIME = 1500; // Milliseconds
const int TURN_TIME = 500; // TUNE ME!
const means this number won't change while the program runs.
The NAME is how the program uses it.
Change the number here, and every move that uses the name changes too.
Notes: TURN_TIME starts at 500 on purpose. It's a guess, and it's almost certainly wrong for your vehicle and your floor. Finding the right number is today's mission.

## Slide 9: The mission lives in setup()
Pathfinder Explorers | Lesson 6
9
e06a_drive_a_square.ino
void setup() {
startRover();
setSpeedLimit(SPEED_LIMIT);
setDriveSpeed(DRIVE_SPEED);
countdown(5); // 5 seconds to step back
// The mission happens ONCE, so it goes in setup().
forward(SIDE_TIME);
spinRight(TURN_TIME);
forward(SIDE_TIME);
spinRight(TURN_TIME);
forward(SIDE_TIME);
spinRight(TURN_TIME);
forward(SIDE_TIME);
spinRight(TURN_TIME);
setAllLights(GREEN); // Mission complete!
}
Notes: Why setup() and not loop()? Ask. (Because we want it to drive the square ONCE. In loop() it would go round and round forever.)
To run it again you switch the vehicle off and on - that restarts the program, and setup() runs again.

## Slide 10: Driving a square, by the clock
Pathfinder Explorers | Lesson 6
10
What you WANT
START
What usually happens FIRST
START
ends up here!
KEY POINT The vehicle can't see where it is. Tiny mistakes add up. Change TURN_TIME by 50 at a time until it comes home.
Notes: Left: what we asked for. Right: what usually happens the first time, when each corner turns a little too little.
Point at the gap at the end of the right-hand path. Nothing is broken - every turn was just a bit short, and the small mistakes added up.
The vehicle has no eyes. It doesn't know it missed. That's the big idea of today: a robot that drives by the clock is only as good as its numbers.
Ask: if the corners were turning TOO FAR, which way would the path go wrong? (It would curl inward.)

## Slide 11
Pathfinder Explorers | Lesson 6
11
Drive a square
About 15 minutes
Autopilot
done
Drive a square
NOW
Tune it
Notes: A breath between parts of the lesson. Read the title out and point at where it sits on the strip.

## Slide 12: Your square
Pathfinder Explorers | Lesson 6
12
PLACEHOLDER
PHOTO: the tape square on the floor, START marked
About 4 feet on a side. An X or an arrow on the START corner showing which way the vehicle faces
Start on the corner, pointing along the tape
Notes: Show how to line up the vehicle: back wheels on the corner, nose pointing exactly along one side. A crooked start makes a crooked square, and that's a variable they should control.

## Slide 13: Drive a square
Pathfinder Explorers | Lesson 6
13
MISSION: e06a_drive_a_square (15 minutes)
Upload it with the wheels UP. The wheels will practice on the stand. That's fine!
Unplug the cable. Power OFF.
Put the vehicle on START, pointing along the tape.
Power ON and step back behind the line. 5-second countdown!
Where did it end up? Mark it with a sticky note.
What you should see
Countdown, four sides and four turns, then green lights
Answer these
Did it come back to START?
Were the corners too much, or too little?
SAFETY Everybody behind the line before the countdown ends. Never grab a moving vehicle - wait for it to stop.
Notes: The first run will almost never come home. Celebrate that - it's what makes the next 20 minutes interesting.
If a vehicle drives straight off the square on the very first side, check SIDE_TIME hasn't been changed, and that the vehicle was pointing along the tape.

## Slide 14
Pathfinder Explorers | Lesson 6
14
Tune it
About 25 minutes
Autopilot
done
Drive a square
done
Tune it
NOW
Notes: A breath between parts of the lesson. Read the title out and point at where it sits on the strip.

## Slide 15: How engineers tune
Pathfinder Explorers | Lesson 6
15
1. PREDICT what will happen.
2. TEST it.
3. MEASURE: where did it end up? Too far, or not far enough?
4. CHANGE ONE THING - like TURN_TIME, by 50.
5. Test again!
KEY POINT Change ONE number at a time. Change two, and you won't know which one helped.
Notes: This is the scientific method in disguise: one variable at a time, everything else the same.
Turns too SHORT means the vehicle under-rotates, so TURN_TIME needs to get BIGGER. Students often get the direction backward the first time; let the next run tell them.

## Slide 16: Tune it
Pathfinder Explorers | Lesson 6
16
MISSION: e06a_drive_a_square (24 minutes)
Turns too SHORT? Make TURN_TIME (line 34) bigger by 50. Too LONG? Smaller by 50.
Write every test in your Mission Log: TURN_TIME, and where it ended up.
LEVEL 2: make the square bigger. Which number do you change?
LEVEL 3: swap the eight moves for a for loop. Then drive a TRIANGLE.
What you should see
Each test ends a little closer to START
Answer these
What's your best TURN_TIME?
Is it the same as other teams'? Why not?
SAFETY Every upload: wheels up, then unplug, then floor.
Notes: Level 2: SIDE_TIME. Level 3: a for loop that runs four times with forward() and spinRight() inside it. A triangle turns 120 degrees at each corner instead of 90, so TURN_TIME becomes about one-and-a-third times as long, and the loop runs three times.
Put every team's best TURN_TIME on the board. They'll all be different - that's the next slide.

## Slide 17: Why isn't every vehicle the same?
Pathfinder Explorers | Lesson 6
17
Every motor is a tiny bit different.
The floor matters: carpet, tile, wood.
The battery matters: a full battery pushes harder.
The vehicle can't SEE where it is. It just counts time.
That's called DEAD RECKONING. Sailors navigated this way for hundreds of years.
KEY POINT Real rovers drive by the clock AND check sensors. Sensors come in the next course!
Notes: Dead reckoning: if you know your speed, your direction and how long you've been going, you can work out where you are - without looking. Ships did exactly this before satellite navigation, and small errors piled up just like today.
Ask: what could the vehicle use to check where it really is? (A camera, a distance sensor, a line on the floor to follow.)

## Slide 18: New words
Pathfinder Explorers | Lesson 6
18
Word | What it means
Autopilot | The vehicle drives a plan by itself
Millisecond | One thousandth of a second. 1000 ms = 1 second
const | A number with a name, that doesn't change while the program runs
Tune | Change a number a little at a time until it works
Dead reckoning | Working out where you are from speed and time, without looking
Notes: Read each word out and have the room say it back. Saying a word out loud is half of owning it.
These are also in the glossary at the back of the Mission Log.

## Slide 19: Check yourself
Pathfinder Explorers | Lesson 6
19
1. How many milliseconds in 2 seconds?
2. What does spinRight(500) do?
3. The corners turn too little. Make TURN_TIME bigger or smaller?
4. Why change only one number at a time?
5. Why might your best TURN_TIME not work on another team's vehicle?
Notes: Answers: 1 2000. 2 spins right on the spot for half a second. 3 bigger. 4 so you know which change made the difference. 5 different motors, battery charge, floor.

## Slide 20: Mission Log, then pack up
Pathfinder Explorers | Lesson 6
20
In your Mission Log
Your tuning table: every TURN_TIME you tried
Circle your best TURN_TIME - you need it next lesson!
Stamp: Autopilot
Pack up
Crew Chief: vehicle power OFF.
Unplug the cable and coil it up.
Vehicle and controller back in their spot, stickers matching.
Close the laptop. Push your chairs in.
KEY POINT Last job: every team member says one thing they learned today.
Notes: Make sure every team has written down its best TURN_TIME. Lesson 7 starts from it.
Batteries: today's floor work drains them. Charge every pack before next lesson.